## Slide 1: WF on Wake-up Signal Design
Qualcomm, Huawei, HiSilicon, …
3GPP TSG RAN WG1 Meeting #91
Reno, USA, November 27 - December 1, 2017
Agenda item 6.2.6.1.1.3

## Slide 2: Background
In RAN1#90bis,
Agreements:
WUS signal is at least cell-specific;
  FFS scrambling of WUS including time varying scrambling
Long ZC sequence based signal is considered as the starting point for WUS signal:
  FFS: whether the sequence can span over multiple subframes
  FFS: whether accumulated multiplication is applied between sub-sequences from the long ZC sequence to reduce the impact of frequency error;
  FFS: Support transmit diversity for NB-IoT WUS
  FFS: NSSS like signal is used as the wake-up signal

## Slide 3: Proposals:
  WUS sequence is a sequence mapping within one subframe and repeated for multiple subframes to support larger coverage.
  WUS sequence is based on ZC-sequence to carry at least partial cell IDs.
  FFS: detailed design on time-varying of the WUS signal