## Slide 1: Discussion on CSI report for SL-CA
April 17, 2024

## Slide 2: Offline discussion
[AT125bis][105][V2X/SL] (Qualcomm)
Scope: To derive majority companies’ view between option 1 and option 2. Also including pros, cons and the corresponding spec impact. Also with the consideration of RAN1 spec and WID.
Intended outcome: Discussion summary in R2-2403927.
Deadline: F2F offline discussion. Date and time will be announced by RRC CR rapporteur. Comeback Thursday session.
At the online session of NR18 SL (Monday, April 15), the following options were discussed
Option 1: Keep the RAN2 agreement.
Option 2: CSI reporting can be only sent on the carrier where CSI reporting REQ is received.

## Slide 3: Technical aspects
For V2X communications, the channel is much more dynamic (much shorter channel coherent time for CSI report) due to the follows.
  More Doppler shift due to dual mobility (relative motion)
  More scattering channel with the by-passed buildings, trees, etc.
UE capability
  Rel-18 SL–CA is intra-ITS band with contiguous carriers, where the Tx UE and Rx UE are expected to have the same capability to support ITS carriers (e.g., based on the regional regulatory rules).
Carrier correlation
  For intra-ITS band, do different carriers have similar radio characteristics?
    No, the radio characteristics can differ. For ITS carriers with only 10MHz bandwidth, frequency selectivity may be observed due to lack of wide enough bandwidth for frequency diversity.
UE1
UE2
Highway Case
60 mile/hour
60 mile/hour
 Performance Observation
  Option 1: may cause more latency for triggering CSI report, since a Tx UE must take turns to trigger CSI report on each carrier, e.g., the Tx UE cannot request CSI report for Carrier #2 till after
    receives CSI report MAC CE for Carrier #1, or
    CSI report MAC CE timer expires for Carrier #1
  Option 2: no extra latency for triggering CSI report, since a Tx UE can trigger CSI report without waiting for the CSI report status on the other carrier.

## Slide 4: WI aspects(RP-230077)
Specify mechanism to support NR sidelink CA operation based on LTE sidelink CA operation [RAN2, RAN1, RAN4]
Support only LTE sidelink CA features for NR (i.e., SL carrier (re-)selection, synchronization of aggregated carriers, power control for simultaneous sidelink TX, packet duplication)
The work is limited to intra-band CA for the ITS band in FR1 (Band n47).
No specific enhancements of Rel-17 sidelink features with sidelink CA support.
This feature is backwards compatible in the following regards
  A Rel-16/Rel-17 UE can receive Rel-18 sidelink broadcast/groupcast transmissions with CA for the carrier on which it receives PSCCH/PSSCH and transmits the corresponding sidelink HARQ feedback (when SL-HARQ is enabled in SCI)
Only Mode 2 operation
Same subcarrier spacing (SCS) among CA carriers to avoid resource selection enhancements and AGC issues
  Time resources for PSFCH are aligned among the carriers for CA
No enhancement related to SCI transmissions on PSCCH/PSSCH, PSFCH transmission, RSRP feedback, CSI feedback and congestion control compared to Rel-16 (i.e., per-carrier operation)
  SL resource indication remains to be per-resource pool and per-carrier basis (no cross-carrier scheduling in SCI)
  UE transmits SL HARQ feedback on the same carrier on which it receives the associated PSSCH
No consideration for limited transmission and reception capability
No primary/secondary carrier differentiation
Reuse the LTE sidelink CA design for the following aspects:
  Sidelink carrier (re-)selection, synchronization of aggregated carriers, Tx power split for simultaneous sidelink transmissions, packet duplication
The CA band combination work in RAN4 is limited to intra-band contiguous CA in Rel-18.
Note: The SL CA work in Rel-18 mainly targets some V2X use cases
i.e., per-carrier == no cross-carrier
e.g., aggregate two 10MHz carriers for total of 20MHz
 WID Observation
  Option 1: allows cross-carrier operation, e.g., not per-carrier
  Option 2: no cross-carrier operation, e.g., only per-carrier.
Votes:
Option 1 is aligned with the WID: Ericsson (1)
Option 1 is not aligned with the WID: LG, HW, Apple, ZTE, NEC, Sharp, AsusTek, OPPO, QC (9)

## Slide 5: Specification aspect
RAN1 specification
  Carrier allocation/selection is limited in RAN2 spec (i.e., MAC).
  Both Option 1 and Option 2 have no impact to RAN1 spec.
  [Nokia]some RAN1 impact, e.g., mention per-carrier. [HW] don’t mention this since it’s RAN1’s decision. [ZTE] just remove this discussion.
RAN2 specification
  Option 1: no spec change to the latest version
  Option 2: may require some spec change since the current spec reflects the RAN2’s agreement (Option 1).
 Specification Observation
  RAN1 spec: both Option 1 and Option 2 have no impact
  RAN2 spec:
    Option 1: no spec change as it is now
    Option 2: need some spec change.

## Slide 6: Options to RAN2 spec
Option A: note
  Option A.1: it’s up to UE implementation how to the UE transmit the CSI MAC CE on the same carrier as CSI report is requested. (Supported: LG preferred, Ericsson, vivo)
  Option A.2: the CSI MAC CE is transmitted with or without data if a grant is available on the same carrier as CSI report is requested; otherwise, carrier (re)selection and resource selection is triggered by the CSI MAC CE.
Option B: normative text
  Option B.1: no LCP update, since MAC CE is not the same as data using LCP, e.g., resource selection with “per-carrier” (Supported: HW, NEC, Nokia, Sharp)
  Option B.2: update LCP for CSI MAC CE (Supported: HW)
  Option B.3: UE transmit … as proposed by ZTE (2643). (Supported: ZTE, HW, Asustek, NEC, Nokia, Ericsson) [OPPO] no strong view, could modify it to make proper UE behaviors. [vivo & Ericsson] prefer stage 2 to avoid too mush spec work. [LG & ZTE] not touch LCP.)
   Prefer no note and no LCP.
 Proposal:
  , option “B.3” is supported for per-carrier SL CSI report.
  Final TP may be handled with other MAC CRs.
If Option 2 is agreed

## Slide 7: TP for SL CSI report
TP (modified ZTE’s 2402642)
5.22.1.7 CSI Reporting
The Sidelink Channel State Information (SL-CSI) reporting procedure is used to provide a peer UE with sidelink channel state information as specified in clause 8.5 of TS 38.214 [7].
RRC configures the following parameters to control the SL-CSI reporting procedure:
- sl-LatencyBoundCSI-Report, which is maintained for each PC5-RRC connection.
The MAC entity maintains an sl-CSI-ReportTimer for each pair of the Source Layer-2 ID and the Destination Layer-2 ID corresponding to a PC5-RRC connection. sl-CSI-ReportTimer is used for an SL-CSI reporting UE to follow the latency requirement signalled from a CSI triggering UE. The value of sl-CSI-ReportTimer is the same as the‎ latency requirement of the SL-CSI reporting in sl-LatencyBoundCSI-Report configured by RRC.
The SL CSI reporting MAC CE corresponding to an SL CSI request is transmitted on the carrier where the SL CSI request is received.
[LG] need this for general coverage. [Nokia] want to limit the change to transmission only as highlighted below.
The MAC entity shall for each pair of the Source Layer-2 ID and the Destination Layer-2 ID corresponding to a PC5-RRC connection which has been established by upper layers:
1> if the SL-CSI reporting has been triggered by an SCI and not cancelled:
2> if the sl-CSI-ReportTimer for the triggered SL-CSI reporting is not running
3> start the sl-CSI-ReportTimer.
2> if the sl-CSI-ReportTimer for the triggered SL-CSI reporting expires:
3> cancel the triggered SL-CSI reporting.
2> else if the MAC entity has SL resources allocated for new transmission on the carrier where the corresponding SL-CSI request is received [Nokia], and the SL-SCH resources on the carrier where the corresponding SL-CSI request is received [ZTE] can accommodate the SL-CSI reporting MAC CE and its subheader as a result of logical channel prioritization:
[Ericsson] Not add it here since this can be for both Mode 1 &2. How about if there is no grant on the wanted carrier? [QC] SL resources here can be triggered by data or CSI MAC CE based resource selection. [Apple, LG, QC, HW, AsusTek] currently CSI MAC CE triggers the resource selection if no grant available due to the latency requirement. May do the same for carrier selection. [Nokia] don’t support CSI MAC CE triggering carrier selection. [Ericsson] we need to think of how to handle this CSI MAC CE triggered carrier selection.
3> instruct the Multiplexing and Assembly procedure to generate a Sidelink CSI Reporting MAC CE as defined in clause 6.1.3.35;
3> stop the sl-CSI-ReportTimer for the triggered SL-CSI reporting;
3> cancel the triggered SL-CSI reporting.
2> else if the MAC entity has been configured with Sidelink resource allocation mode 1:
3> trigger a Scheduling Request.
NOTE 1: The MAC entity configured with Sidelink resource allocation mode 1 may trigger a Scheduling Request if transmission of a pending SL-CSI reporting with the sidelink grant(s) cannot fulfil the latency requirement associated to the SL-CSI reporting.
NOTE 2: Regardless of a carrier that receives an indicator triggering SL-CSI reporting in the SL Carrier Aggregation, it is up to UE implementation to decide which carrier the UE sends SL-CSI reporting MAC CE.