## Slide 1: Recommendation for R2D triggering for Msg1 resources in A-IoT random procedure
R2-2501498
Agenda Item: 8.2.2
Source: Huawei, HiSilicon
3GPP TSG-RAN WG2 Meeting #129
Athens, Greece, 17th – 21st February, 2025

## Slide 2
Introduction
  TR 38.769: A R2D transmission triggering random access determines X time domain resource(s) for D2R transmission(s) for Msg1, where each D2R transmission for Msg1 occurs in one time domain resource of the X time domain resource(s).
  Proposal: From RAN2 perspective, the R2D transmission, which determines the Msg1 time resource(s), can be achieved by the below two ways, unless RAN1 concludes to use L1 signaling later:
      Way-1: introducing new R2D message other than the paging message, e.g., QueryRep-like; or
      Way-2: reusing the same paging message format, using field(s) to indicate it is only to determine the Msg1 time resource(s) and omitting the paging identifier (device ID/group ID) field.
Recommendation