## Slide 1: SL RESOURCE RESELECTION IN CASE OF lbt FAILURE

## Slide 2: ISSUE
As captured in clause 5.22.1.2c of TS 38.321, how a UE performs resource re-selection if the UE has been configured with resource allocation mode 2 in an unlicensed carrier, is described as the above
Whether is the selected number of HARQ retransmissions always used for resource reselection in case of LBT failure is triggered for the resource/transmission opportunity?

## Slide 3: RAN2 agreements on MCST
Agreements on MCSt resource (re)selection triggering:
  Working assumption (Trigger resource (re)selection if all initial transmission and retransmission within MCSt fail due to LBT failure. It should provide minimum specification change.) is confirmed.
  It is captured in clause 5.22.1.2 as shown in the below
1> if a MAC PDU is not transmitted (i.e. initial transmission or retransmission) in any of the resources for this MAC PDU that are associated with the sidelink process for Multi-consecutive slots transmission due to the Sidelink LBT failure:
NOTE 2: If the remaining PDB is not met, it is left for UE implementation whether to perform transmission(s) corresponding to single MAC PDU or sidelink resource reselection.
NOTE 3: It is left for UE implementation whether to trigger the TX resource (re-)selection due to the latency requirement of the MAC CEs triggered according to clause 5.22.1.7 and clause 5.22.1.10.1.
2> if multiple carrier frequencies are configured:
3> trigger the TX carrier (re-)selection procedure as specified in clause 5.22.1.11.
NOTE 3a: It is up to UE implementation to avoid triggering the TX carrier (re-)selection procedure again if it has just performed TX carrier (re-)selection procedure.
2> clear the selected sidelink grant associated to the Sidelink process, if available;
2> trigger the TX resource (re-)selection

## Slide 4: Way forward/conclusion
Proposal 1: In the current MAC procedure specified in clause 5.22.1.2c (which is specified for non MCSt case), “the selected number of HARQ retransmissions” need to be deleted in the procedure texts.
Proposal 2: add a note in clause 5.22.1.2c stating that the procedure specified in clause 5.22.1.2c is only applicable for non MCSt. FFS if more changes are needed for the case of multiple TB MCSt using single slot candidate resources.
Proposal 3: add “as specified in clause 5.22.1.1” in the procedure texts in clause 5.22.1.2

## Slide 5: THANK YOU
Min Wang
Ericsson