## Slide 1: Data forwarding on Inter-system HO
NTT DOCOMO, INC.
R3-186614
3GPP TSG-RAN WG3 RAN3#102
Spokane, Washington, USA, 12th Nov 2018 - 16th Nov 2018

## Slide 2: Background
Data forwarding on Inter-system HO is discussed for a long time.
However, there still be three options as described in [1].
  Solution 1 in [2], Solution 2 in [3] and [4], Solution 3 in [5]
This paper provides illustrates those options and way forward from operator perspective.

## Slide 3: Case 1: Intra-system handover
Forwarding Tunnel
- per DRB for PDCP SDU
- Per PDU session for fresh packet
End Marker
- Per tunnel (for DRB tunnels)
- Per tunnel (for PDU session tunnels)
UPF
Target
RAN
1
Source
RAN
2
Tunnel
- Per PDU session
End Marker
- Per tunnel
Following was already agreed.
  Note that not only Xn HO but also NG HO same would be applied.

## Slide 4: Case 2: Inter-system handover (5G => 4G)(1/2)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
UPF
Target
RAN
1
2
GW
Source
RAN
3
4
Tunnel
- Per PDU session
End Marker
- Per tunnel
Solution 1
3 proposed solutions captured (red text shows difference)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per PDU session (for 2)
- Per tunnel (for 3 & 4)
UPF
Target
RAN
1
2
GW
Source
RAN
3
4
Tunnel
- Per PDU session
End Marker
- Per tunnel
Solution 2

## Slide 5: Case 2: Inter-system handover (5G => 4G)(2/2)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per tunnel (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per tunnel (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per tunnel (for 2)
- Per tunnel (for 3 & 4)
UPF
Target
RAN
1
2
GW
Source
RAN
3
4
Tunnel
- Per PDU session
End Marker
- Per tunnel
Solution 3

## Slide 6: Case 3: Inter-system handover (4G => 5G)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3)
- Per E-RAB (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3)
- Per E-RAB (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
Forwarding Tunnel
- Per E-RAB (for 2 & 3)
- Per PDU session (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
Forwarding Tunnel
- Per E-RAB (for 2 & 3)
- Per PDU session (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per QoS flow (for 4)
Forwarding Tunnel
- Per E-RAB (for 2 & 3)
- Per PDU session (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per QoS flow (for 4)
Forwarding Tunnel
- Per E-RAB (for 2 & 3)
- Per PDU session (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per QoS flow (for 4)
GW
Target
RAN
1
2
UPF
Source
RAN
3
4
Tunnel
- Per E-RAB
End Marker
- Per tunnel
GW
Target
RAN
1
2
UPF
Source
RAN
3
4
Tunnel
- Per E-RAB
End Marker
- Per tunnel
Solution 2
Solution 1
3 proposed solutions captured (red text shows difference)

## Slide 7: Case 3: Inter-system handover (4G => 5G)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3)
- Per E-RAB (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3)
- Per E-RAB (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3)
- Per E-RAB (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
GW
Target
RAN
1
2
UPF
Source
RAN
3
4
Tunnel
- Per E-RAB
End Marker
- Per tunnel
Solution 3

## Slide 8: Summary of options
There would be some difference on impact for nodes (i.e. UPF and/or NG-RAN.)
However, only Option 3 enables direct data forwarding (if there is direct path between source RAN node and target RAN node.)
To minimize the interruption time, it would be better to enable direct data forwarding as direct data forwarding would have less interruption time.
Furthermore, in-direct data forwarding is inefficient if one physical RAN node connects to both EPC and 5GC.
  On direct data forwarding, data would be forwarded within the node.
Next slide illustrates further on the interruption time.

## Slide 9: Interruption time on inter-system HO
To minimize interruption time, some data needs to be arrived before 10.
However, the time period from 8 to 10 would be very short as it is just between RAN node and UE. (i.e. No need to involve CN.)
On the other hand, indirect data forwarding may take more time in some deployment as it requires (both) CN involvement.
Thus, direct forwarding would be required to minimize interruption time.
UE
RAN node
In CN1
9. RACH procedure
CP for CN2
(MME or AMF)
RAN node for CN2
UP for CN2
(SGW or UPF)
CP for CN1
(MME or AMF)
UP for CN1
(SGW or UPF)
1.Measurement report
2.HO Required
3. Relocation req.
4.HO req.
5.HO req. ACK
6.Relocation resp.
7.HO Command
8.HO Command
(RRC Reconf.)
10.HO Complete
(RRC Reconf. Comp.)
DL Data
Indirect data forwarding
Direct data forwarding
Minimum
interruption
time

## Slide 10: Proposed Way forward
RAN3 to apply Solution 3 described in [5]

## Slide 11: Reference
[1] RAN3_101bis_agenda_with_Tdocs_20181012_EOM.doc
[2 ]R3-186128,,
[3] R3-186127, “(TP for NR BL CR for TS 38.300): Handling of Inter-system end markers (Solution 2)” , Nokia, Nokia Shanghai Bell
[4] R3-186256, “(TP for NR BL CR for TS 38.300): Handling of Inter-system end markers ”, Nokia, Nokia Shanghai Bell
[5] R3-186129, “TP for BL CR for 38.300 for inter-system HO” , Ericsson, Nokia