## Slide 1: Rel-17 FR1 RF enhancement part 1 GTW status
Moderator (Huawei, HiSilicon)
3GPP TSG-RAN WG4 #100-e
August 16 – 27, 2021
Electronic meeting

## Slide 2: Agenda
PC2 Intra-band UL NC CA
Intra-band UL contiguous CA for UL MIMO
Scell dropping

## Slide 3: Background for intra-band UL NC CA
Arch | description
#1 | 2x26dBm PA + 2LO with 100MHz BW
#2 | 1x26dBm PA + 1LO with 200MHz BW
#3 | 2x23dBm PA + 1LO with 200MHz BW
#4 | 1x23dBm+1x26dBm + 2LO with 100MHz BW
Table: 4 architectures for intra-band UL NC CA under discussion

## Slide 4: Sub topic 2-1: MPR comparison among architecture options
Issue 2-1-2: whether MPR requirements are separate defined for different architecture?
Option 1: (2 companies)
  Architecture #2 and #3 will use separate MPR values in the specification (table or delta) and address both TxD and UL MIMO modes.
  For architecture #1 and #4, General MPR table is based on the 2LO 2xPC2 PA architecture and a 1.5dB additional MPR allowed for 2LO PC3+PC2 architecture
Option 2: (1 company)
  RAN4 will specify the one MPR Table to support the PC2 simultaneous UL CA + UL MIMO with 2 transmit for 1 LO RF architecture.
  RAN4 will specify the one MPR Table to support the PC2 intra-band NC-CA UE for 2 Los RF architecture based on the #4 RF architecture.
Option 3: (2 companies)
  Define one set of MPR across 4 architectures, use the worst case value across architectures to define MPR for non-contiguous CA
Option 4(1 company, during discussion):
  MPR can be different based on dualPA and dualPA is coupled with number of LO’s.
  Moderator note: it means one set MPR for arch #1 and #4, and one set MPR for arch#2 and arch#3.
  Architecture #2 and #3 should have same MPR table.
  For MPR set of arch#1 and #4, arch #1 should be baseline.
  CA+UL MIMO should be handled in the part for UL CA + MIMO

## Slide 5: Sub topic 2-1: MPR comparison among architecture options
Issue 2-1-1: MPR comparison across architecture based on all inputs
MPR |  | HW R4-2114494 |  |  |  | Nokia R4-2112022 | LGE R4-2109965 |  | Skyworks R4-2104819 |  | Current PC3 requirement | WC Across 4 architectures | WC For #1 and #4 set | WC For #2 and #3 set
IM3 region | B | Archi#1 | Archi#2 | Archi#3 | Archi#4 | Archi#2 | Achi#1 | Achi#4 | Achi#1 | Achi#4 | 2PA Achi |  |  | 
-30dBm/MHz | 0.72 | 14.5 | 15.1 | 15.6 | 14.7 | 14 | 15 | 16 | 5.1 | 7.1 | 15 | 16 | 16 | 15.6
 | 1.44 | 11.3 | 12.8 | 13 | 11.4 |  | 14 | 15 | 4.9 | 6.7 | 14.5 | 15 | 15 | 14
 | 2.88 | 11.2 | 12.5 | 12.5 | 11.4 | 14.4 | 12.5 | 14 | 4.3 | 6.3 | 13.5 | 14 | 14 | 14.4
 | 5.76 | 10.7 | 11.2 | 11.3 | 10.8 | 12.5 | 10.5 | 12 | 3.5 @5.4M | 5.7@5.4M | 11.5 | 12.5 | 12 | 12.5
 | 10.8 | 10.2 | 11 | 11.4 | 10.5 | 10.8 | 10 | 10.5 | 2.6 @11.52M | 4.9@11.52M | 10.5 | 11.4 | 11.4 | 11.4
 | 23.04 | 9.2 | 10.5 | 10.7 | 9.5 | 6.7 | 8.5 | 9 |  |  | 9 | 10.7 | 9.5 | 10.7
 | 46.08 | 8.8 | 9.4 | 9.7 | 8.9 | 5.6 |  |  | 4.7 | 6.8 |  | 9.7 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 9.7
 | 92.16 | 8.5 | 8 | 8.3 | 8.7 | 4.78 |  |  | 1.7@77.7M | 4.5@77.7M |  | 8.7 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8.3
 | 97.92 | 8.3 | 8.9 | 9.3 | 8.5 | 4.67 |  |  |  |  |  | 9.3 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 9.3
 | 103.68 | 8.1 | 9.5 | 9.9 | 8.3 | 4.57 |  |  |  |  |  | 9.9 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 9.9
 | 116.64 | 7.5 | 8.3 | 8.7 | 7.8 | 4.33 |  |  |  |  |  | 9 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8.7
-13dBm/MHz | <0.54 | 7 | 8.5 | 8.3 | 7.2 |  |  | 9 |  |  | 9 | 9 | 9 | 8.5
 | 0.54 | 6.8 | 8 | 7.5 | 7 |  |  | 8 |  |  | 8 | 8 | 8 | 8
 | 1.08 | 6.5 | 8 | 7.5 | 6.8 |  |  | 7 |  |  | 7 | 8 | 7 | 8
 | 2.16 | 6.5 | 7.5 | 7.2 | 6.6 |  |  | 6.5 |  |  | 6.5 | 7.5 | 6.5 | 7.5
 | 3.24 | 6 | 7.3 | 7 | 6.3 |  |  | 5.5 |  |  | 5.5 | 7.3 | 6.3 | 7.3
 | 5.4 | 5.5 | 6.4 | 5.7 | 5.8 |  |  | 4 |  |  | 4 | 6.4 | 5.8 | 6.4
 | 10.8 | 3.2 | 4 | 3.8 | 3.3 |  |  | 4 |  |  | 4 | 4 | 4 | 4

## Slide 6: Sub-topic 2-2: Other requirements related to different Architectures
Arch | description | Additional RF requirement need to be considered
#1 | 2x26dBm PA + 2LO with 100MHz BW | 
#2 | 1x26dBm PA + 1LO with 200MHz BW | In-gap requirement when LO or image fall inside
#3 | 2x23dBm PA + 1LO with 200MHz BW | In-gap requirement when LO or image fall inside
#4 | 1x23dBm+1x26dBm + 2LO with 100MHz BW | PA swap time
Issue 2-2-1: For 1x26dBm PA + 1LO with 200MHz BW and 2x23dBm PA + 1LO with 200MHz BW, how to handle in-gap requirement when LO or image fall inside?
Option 1: (4 companies)
  No OOBE exception requirement for architecture #2 and #3, use moderate MPR to reach the in-gap requirement
  Assume IQ suppression>=32dBc, LO leakage>=35dBc
Option 2: (3 companies)
  In-gap exceptions are only allowed for CC configurations where the gap bandwidth is less or equal than the two CC aggregated bandwidth thus SEM is -13dBm/MHz in gap and shall be met
  3dB ACLR in gap relaxation is allowed and assumes
  In-gap exceptions are only allowed for UEs also supporting UL MIMO or TxD together with NC UL CA

## Slide 7
    Sub-topic 2-2: Architecture options handling
Issue 2-2-2: For 1x23dBm + 1x26dBm PA + 2LO with 100MHz BW, how to handle the swap time between PAs?
Option 1: 15us only for:
  case1 and case2/3,
  case2 and case3
  where:
  Case1 is that the transmission power for both CCs are ≤23dBm.
  Case 2 is that the transmission power for CC1 is larger than 23dBm and for CC2 is ≤23dBm, while case 3 is that the transmission power for CC2 is larger than 23dBm and for CC1 is ≤23dBm.
Option 2: RAN4 do not need to define the additional swapping time requirements for #4 RF architecture. (Because it is corner case to configure Scell with maximum transmission power since the NW expected that the UE is located in cell boundary.)
Option 3: A maximum swap time of 15us – MRTD is allowed
    Both SCC and PCC shall be able to reach maximum power for equal PSD case with large allocation difference
Discussion status:
Question1: Can we agree, PA swapping case is corner case in real network?
Reasons provided in LGE contribution R4-2112893:
Observation 1: it is not general use case for intra-band NC CA operation when NW is deployed in co-located scenarios (MRTD is less than 10~15 us).
Observation 2: it is corner case to configure Scell with maximum transmission power since the NW expected that the UE is located in cell boundary. So the Scell can be released.
Question2: if it is corner case, can we agree not to introduce the swapping time?

## Slide 8: Contiguous CA+MIMO

## Slide 9: Sub topic 3-1: RF requirements
Issue 3-1-1: MPR requirement for PC3 UL contiguous CA +MIMO with 2 PC3 PA+1LO
Proposals
  Option 1: Adding 0.5dB delta MPR on outer allocation(outer1 and outer2 for NC allocation, outer for C allocation) based on the MPR defined for PC3 contiguous CA. (3 companies)
  Option 2: Reuse the MPR for PC3 contiguous CA with 1Tx (4 companies)
Potential WF: Reuse the MPR for PC3 contiguous CA with 1Tx as a starting line.

## Slide 10: Sub topic 3-1: RF requirements
Issue 3-1-2: MPR requirement for PC2 UL contiguous CA +MIMO with 2 PC2 PA+1LO or 2 PC3 PA+1LO
Proposals
  Option 1: Adding 0.5dB delta MPR on outer1 and outer2 allocation based on the MPR defined for PC2 contiguous CA with 1PA.(3 companies)
  Option 2: an additional 0.5 to 1dB MPR can be anticipated for PC2 contiguous UL CA realized with 1LO+2xPC3 PA compared to agreed MPR for 1LO/1PA PC2 case(for all allocations) (1 company)
  Option 3(during discussion): No additional MPR compared with 1Tx PC2 contiguous CA is needed (1 company)

## Slide 11: Sub topic 3-2: signalling
Issue 3-3-1: Signalling problems
1: In currently capability definition, if UL-MIMO support were reported in the CCs for CA, theoretically CA and UL-MIMO should be supported simultaneously unless stated otherwise.
For better understanding, copy more from vivo contribution who raise this problem:
Observation 3: There exists some architecture, though not necessarily typical, can support CA and UL-MIMO respectively but not simultaneously. These implementations are somewhat contradicting with current signalling scheme.
Observation 4: Keep current signalling unchanged may preclude some implementations which is not typical.
2: There is only one ca-BandwidthClassUL-NR capability reported for each BC entry, and RAN2 NW is not required to derive UE capability based on multiple band combination entries.
3: Reporting different aggregated CBW in two band combinations for CA only and CA+UL MIMO is not feasible.

## Slide 12: Sub topic 3-2: signalling
Issue 3-2-2: Signalling proposals
Proposals
Option 1: Introduce a separate bandwidth class capability for UL-MIMO(1 company)
Option 2: Report the UE supported aggregated CBW for UL CA+UL MIMO feature to NW(2 companies)
Option 3: Whether develop new signalling for support of CA + UL-MIMO drives by implementation(1 company)
      Yes. Incorporate implementations with narrowband PA.
      No. Preclude implementation with narrowband PA
Option 4: No need to introduce new signalling(3 companies)

## Slide 13: Scell dropping

## Slide 14: Sub topic 4: Scell dropping
Issue 4-1-2: RAN1 or RAN4 driven?
Proposals
  Option 1: If SCell dropping in UL CA would be confirmed as a real field issue, RAN1 should be involved in any specification alteration on the intent to mitigate this issue.(2 companies)
  Option 2: RAN4 driven, but ask RAN1 to confirm that there is no impact on the RAN1 specifications. (4 companies)

## Slide 15: Sub topic 4: Scell dropping
Issue 4-1-3: Release issue
Proposals
  Option 1: the solution targets for Rel-16
  Option 2: the solution is newly studied in Rel-17.
It seems all companies can accept option 2 in 1st round discussion.
Tentative agreement: option 2

## Slide 16: Sub topic 4: Scell dropping
Issue 4-2-3: What is the frequency range that the solution should work for?
Proposals
  Option1: Both FR1 and FR2(7 companies)
  Option 2: FR1 with higher priority(1 company)
  Option 3: other

## Slide 17: Sub topic 4: Scell dropping
Issue 4-2-1: RAN4 driven solutions proposed
Proposals
  Option 1: solution as in R4-2112826: RRC configuration +MAC activation onΔPCMAX,f,c , and introduce this config into Pcmax definition for SC and CA
  Option 2: solution as in R4-2114551: new parameter that indicates UE the preferred priority of cells
  Option 3: other