## Slide 1: Resolving the Scell dropping using power limits on serving cells
[99-e][127] NR_RF_FR1_enh_Part_1_HPUE_ULMIMO
Ericsson
3GPP TSG-RAN WG4 Meeting #100-e
Electronic meeting, 16 – 27 August 2021
26 May 2021

## Slide 2: Background
For any CA band combination, the UE configures
  a configured maximum output power PCMAX,f,c for each serving cell c of the configuration
  a configured maximum output power PCMAX for the total power of the configuration
When the PCMAX is exceeded, the UE prioritizes the transmissions according to the rules in clause 7.5 of 38.213
Configure in RRC relative UE-specific limits on DPCMAX,f,c on PCMAX,f,c on one or more of the serving cells c
Can be enabled/disabled by MAC-CE for fast adaptation
Only applies for concurrent transmissions
  If only high priority transmission scheduled this would get all available power up to PCMAX

## Slide 3: No limits: dropping or scaling Scells
PCell
PUSCH
Scell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
Ppower class
Reduced or dropped
PCMAX,f,c
PPUSCH,f,PCell
PPUSCH,f,SCell
The intra-band case shown above

## Slide 4: Limit on Pcell and the Scell scaled
PCell
PUSCH
Scell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
DPCMAX,f,PCell
PPUSCH,f,PCell = PCMAX,f,Pcell (reduced)
Ppower class
PPUSCH,f,SCell
PCMAX,f,SCell
The UE may still drop the Scell (no restriction in 38.213)

## Slide 5: Limit on both cells, dropping will not occur
PCell
PUSCH
Scell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
DPCMAX,f,Pcell = DPCMAX,f,Scell = 3 dB
Ppower class
The actual UE back-off can be any value, both cells are still 3 dB below

## Slide 6: If only one cell scheduled, limits do not apply
PCell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
DPCMAX,f,Pcell = DPCMAX,f,Scell = 3 dB
Ppower class
No other transmission overlapping a slot of a scheduled transmission
Reduces the need for enabling/disabling limits by MAC-CE signaling

## Slide 7: Summary
The solution feasible for both FR1 and (at least for intra-band for) FR2
RAN1 impact to be confirmed
Solved the ”equal PSD” issue in RAN5
...and can also be used in the field

## Slide 8: References
R4-2112826, “Resolution of the Scell dropping (power reduction) problem”, Ericsson
[R4-2112811, “Introduction of power limits for serving cells of UL CA” (FR1), Ericsson
[R4-2112816, “Introduction of power limits for serving cells of UL CA” (FR2), Ericsson