3GPP TSG-RAN WG4 Meeting # 102-e 												R4-220xxxx

Electronic Meeting, February 21st – March 3rd , 2022

Agenda item:	10.5.1

Source: 	Qualcomm Incorporated

Title: 	WF on TDD Repeater Switching

Document for:	Approval

# Introduction

This document provides a WF on TDD Repeater Switching.

# Way Forward

## Group Delay Handling

Agreement:

Whether group delay needs to be known for conformance testing (e.g. for EVM test) will be discussed during the conformance test

Companies proposing that group delay needs to be known should bring contributions show why this is necessary.

## Switching time accuracy testing

Agreement:

A single EVM test is needed to check the timing accuracy and that EVM requirements are met.

## EVM Requirement and Transitions

Agreements:

EVM requirement/test should include the symbol just before the transition (as is the case for the BS requirement).

No additional EVM requirement will be defined for symbols before the transitions. There is no need for any special handling during the test for the symbol before transitions.

## Definitions related to TDD Operations

Agreements:

Definitions for repeater ON, OFF and transient period to be captured in the specifications.

Baseline for the definitions, to be further checked/refined:

•	Repeater OFF period: “time period during which the repeater downlink or uplink is not allowed to transmit in the corresponding direction”;

•	Transmitter ON period: “time period during which the repeater downlink or uplink is transmitting in the corresponding direction”;

•	Transmitter transient period: “time period during which the transmitter is switching from the OFF period to the ON period or vice versa”

## Handling of Long Delay Repeater

Agreements:

The extended group delay and deployment restrictions are indicated by vendor declaration. Details will be discussed in the conformance phase, there is no need to capture anything related to this in the core specifications.

The declared group delay is separate from the transient times defined in the core specifications. The declared group delay will be taken into account separately in conformance testing (group delay will be added to the transient times to compute the overall transient time of the repeater).

There is no need for any special handling of the long delay repeater in the specifications. Also, no new interface is needed for such a repeater.

## TDD Switching Diagram

Agreement:

The switching diagram to be captured in the spec:

Figure X.X

Note 1. DL/UL transmission in the diagram denotes either UL or DL transmission not simultaneous DL/UL transmission

Note 2. The transition off/on and on/off is triggered by a change in the direction of the input signal

Note 3. On power level for DL and UL can be different

# Comments

should we use “repeat” or “forward” instead of transmit?

should we use off state and on state instead of period?

There was no clear consensus on this issue, please check if this is clear enough or rewording/further clarification is needed.