## Slide 1: Motivation for updating the scope of the basket WI adding new channel BW in existing bands
Ericsson
RP-230417
3GPP TSG-RAN Meeting #99
Rotterdam, Netherlands, March 20-23, 2023
Agenda item: 9.4.5.4

## Slide 2: Background
When the basket WI to add new channel BW in existing NR bands was agreed, CA and EN-DC was out of scope.
  The intention with this was to avoid introducing new CA or EN-DC combinations via this basket WI, this should be done via the CA/EN-DC basket WIs.
In Rel-17, new BCS4 and BCS5 were introduced.
  BCS4 and BCS5 contain all possible defined channel bandwidths for each band in the combination.

## Slide 3: Motivation
When a new channel BW is added to an existing NR band, this channel BW is automatically added to the BCS4/BCS5 combinations for that band. But the MSDs for that channel BW and BCS4/BCS5 combinations should also be checked and updated when:
  The new BW is the new highest BW of an aggressor band for crossband isolation (note that it may also create an MSD where there was no MSD before).
  The new BW is the new smallest BW of a victim band of an existing MSD.
This task is currently not covered by any WI.
Proposal: Update the new channel BW basket WI to explicitely include this task in the scope.