## Slide 1: On changes of the regulation in Japan
SoftBank Corp., NTT docomo INC, KDDI Corporation, Rakuten Mobile Inc.,
3GPP TSG-RAN WG4 Meeting #108
Toulouse, FR, August 21st – 25th , 2023
Agenda Item: 13 (AOB)
Document for: Information
R4-2311288

## Slide 2: Introduction
This paper is intended to introduce changes of the domestic regulation in Japan.
The contents in this material are limited to 3GPP RAN4 impacted items:
  B28 3MHz in LTE [1]
  Relaxation of PHS protection in LTE/NR [2]
  HP-UE related (NR, CA/DC, EN-DC, FR2) [2]
The official dates of publishing the regulations are TBD.
For an individual item, the relevant proponent provides (or has provided) proposals/discussion papers

## Slide 3: 3MHz LTE allocation in B28
B28 3MHz is on a fast track:
  The following ranges are to be allocated
  UL: 715-718MHz, DL: 770-773MHz
  Relevant contributions are to be submitted
  No UE co-ex regulation to DTV is defined for this range but BS deployment plan is to be inspected to mitigate interference
  3GPP’s confirmation of possible interference level to DTV region is quite helpful for the practical deployment/operation
In the regulation, 3MHz LTE is allowed in the range of B28, B26, B8 and B3
NR regulation is postponed until 3GPP concludes a set of general requirements for 3MHz CBW.

## Slide 4: PHS protection relaxation(LTE/NR)
While PHS service is terminated, the protection requirement is not solely removed but largely relaxed (for digital codeless phones). New requirements are:
  For UE in 5MHz CBW in B1/n1: -25dBm/MHz@1910–1915.7MHz, -30dBm/MHz@1884.5-1910MHz
  For UE in 10MHz or larger CBWs in B1/n1: -25dBm/MHz@1906.6–1915.7MHz, -30dBm/MHz@1884.5-1906.6MHz
  Note that for UE other than in Band 1/n1, -30dBm/MHz@1884.5 – 1915.7MHz is applied
Also note that BS protection requirement is kept as it is (-41dBm/300kHz), even from bands other than B1/n1

## Slide 5: HP-UE(NR) – FR1
For TDD single bands: n41, n77/n78, n79
  29dBm is allowed, except 4000-4100MHz (against Altimeter) and 4600-4800MHz (Local 5G/indoor)
  Note that n40 is not for HP-UE this time
  For n41, discussion in 3GPP is ongoing for 30MHz CBW A-MPR
  No other impacts are foreseen in 3GPP
For inter-band CA/DC (including EN-DC)
  The sum of MOP of two bands are allowed for inter-band two bands UL scheme
  No impact is foreseen in 3GPP: the relaxation can be understood looser than current 3GPP schemes where upper bound is still limited to PC1.5 or PC2 in general

## Slide 6: HP-UE(NR) – FR2
For bands n257/n258
UE max power limit is expanded to 35dBm(TRP) and 55dBm(EIRP)
  FR2 PC1 is allowed in Japan
  No impact is foreseen in 3GPP

## Slide 7: APPENDIX: Future spectrum assignment
New spectrum assignment is expected to be done by the end of March 2026 [3].
Candidates of frequency ranges are:
  4.9-5.0GHz(n79)
  25.25-27.0GHz(n257, n258)
  37.0-43.5GHz(n259, n260)

## Slide 8: References
[1] https://www.soumu.go.jp/main_content/000887877.pdf
[2] https://www.soumu.go.jp/main_content/000887872.pdf
[3] https://www.soumu.go.jp/main_content/000846639.pdf
(Ref [1], [2] and [3] are written in Japanese)