## Slide 1: NR RRM enhancements in Rel-19
3GPP TSG RAN Rel-19 workshop R4-2313528
Toulouse, France, August 21-25, 2023
Agenda Item: 12
Source: Ericsson
Title: NR RRM enhancements in Rel-19
Document for: Information

## Slide 2: Contents
FR2 Layer-3 measurement delay reduction
UE power saving enhancements

## Slide 3: FR2 Layer-3 measurement delay reduction
Justification
FR2 measurement delay for layer-3 measurements (e.g. cell search, RSRP/RSRQ/SINR period) is much longer than in FR1 due to UE RX beam sweeping.
Rel-18 work on FR2 delay reduction is limited to SCell activation.
FR2 measurement delay increases execution of mobility procedures which rely on Layer-3 measurements.
Longer measurement delay causes more scheduling restriction resulting in throughput loss.
Wide range of UEs are expected to support simultaneous reception of reference signals (e.g. SSB, CSI-RS) from multiple beams and cells by means of utilizing multi-Rx chain/multi-panel implementation.
Objectives
  FR2 measurement delay reduction for layer-3 measurements [RAN4]
    Identify cases where FR2 delay can be reduced at least for the following layer-3 measurements (intra/inter-frequency/inter-RAT NR/CA/DC) applicable in all the relevant RRC states: RRC Idle, RRC inactive and RRC connected states:
      RRC idle/inactive: cell re-selection, including idle mode CA/DC measurements etc.
      RRC connected: RLM, beam management/link recovery procedure, cell search, RSRP/RSRQ/SINR, SSB index acquisition, CGI reading etc.
    Specify reduced measured delay requirements for the identified cases
  Specify if needed, signaling enhancement for the UE to meet the reduced FR2 delay requirements [RAN4, RAN2]
  Specify RRM performance requirements including test cases for the above core requirements [RAN4].
BS1
Cell change
BS2
Mobility procedures rely on layer-3 measurements

## Slide 4: UE power saving enhancements
Justification
eDRX and relaxed RLM/BFD measurements enable substantial UE power saving without impacting network performance when used in certain scenarios.
In LTE eDRX requirements are specified for all types of UEs and in all RRC states.
eDRX requirements are specified only for Redcap UE in RRC idle and RRC inactive states since Rel-17.
RLM/BFD measurements for NR UEs can be relaxed under certain conditions e.g. low mobility, high SNR
  However, relaxed RLM/BFD requirements are not specified for Redcap
Objectives
eDRX requirements for all type of NR UEs [RAN4]
  Specify measurement requirements for eDRX cycle for all type of NR UEs (except RedCap) in:
    RRC idle state and
    RRC inactive state
Relaxed RLM/BFD requirements [RAN4]
  Identify cases where SSB/CSI-RS based RLM/BFD measurements can be relaxed for Redcap UE.
  Specify relaxed RLM/BFD requirements for Redcap UE for SSB/CSI-RS based RLM/BFD for the identified cases.
Specify RRM performance requirements including test cases for the above core requirements [RAN4].
eDRX cycle
Time
DRX cycle

PTW



Paging time window (PTW) of eDRX contains multiple DRX cycles
SSB periodicity
Time
Example of SSBs used for relaxing RLM/BFD


UE sparsely uses configured SSBs for relaxed RLM/BFD measurements to conserve its power