## Slide 1: Clarification on the band-ordering based approach
MediaTek Inc.
3GPP TSG-RAN WG4 Meeting #108
Toulouse, France, August 21 – August 25, 2023
Agenda Item: 8.23.4
R4-2314765

## Slide 2
Per-Tx-chain-based switching representation
The order of four bands in the signaling indicates a per-tx-chain-based switching
  At Tx Chain#1, band A (switch-from) switched to band C (switch-to)
  At Tx Chain#2, band B (switch-from) switched to band D (switch-to)

## Slide 3
3
Example: UE preferred Tx switching
UE to enable the band ordering approach only if the preferred Tx switching has an improved switching period compared with that for non-preferred Tx switching. In this case, it means:
max(Tswitch_A-C,Tswitch_B-D) < max(Tswitch_A-C,Tswitch_B-D ,Tswitch_A-D, Tswitch_B-C) = max(Tswitch_A-D, Tswitch_B-C)

## Slide 4
Case 1, UE granted with preferred Tx switching

## Slide 5
How it works for Case 1
Step 1: UE reports its preferred switching via “per-Tx-chain-based representation”for band combination (A,B,C,D)
Step 2: NW schedule a Tx switching as UEs preferred switching and sends the scheduled switching configuration to UE via “per-Tx-chain-based representation”
Step 3: UE performs the granted Tx switching, where the switching period is improved as:
    min {max(Tswitch_A-C,Tswitch_B-D), max(Tswitch_A-D, Tswitch_B-C)}
    = max(Tswitch_A-C,Tswitch_B-D)

## Slide 6
6
Case 2, UE granted with non-preferred Tx switching

## Slide 7
How it works for Case 2
Step 1: UE reports its preferred switching via “per-Tx-chain-based representation”for band combination (A,B,C,D)
Step 2: NW schedule a Tx switching as none UEs preferred switching and sends the scheduled switching configuration to UE via “per-Tx-chain-based representation”
Step 3: UE performs the granted Tx switching, where the default switching period applies:
    max {Tswitch_A-C,Tswitch_B-D, Tswitch_A-D, Tswitch_B-C}
    = max{Tswitch_A-D, Tswitch_B-C}