## Slide 1: Clarification on the band-ordering based approach
MediaTek Inc.
3GPP TSG-RAN WG4 Meeting #108
Toulouse, France, August 21 – August 25, 2023
Agenda Item: 8.23.4
R4-2314859
Rev of R4-2314765

## Slide 2
Per-Tx-chain-based switching representation
The order of four bands in the signaling indicates a per-tx-chain-based switching
  At Tx Chain#1, band A (switch-from) switched to band C (switch-to)
  At Tx Chain#2, band B (switch-from) switched to band D (switch-to)

## Slide 3
3
Example: UE preferred Tx switching
UE may to enable report the optional band ordering approach only if the preferred Tx switching has an improved switching period compared with the base line (i.e., max(Tswitch_A-C,Tswitch_B-D ,Tswitch_A-D, Tswitch_B-C))that for non-preferred Tx switching. In this case, it means:
max(Tswitch_A-C,Tswitch_B-D) <= max(Tswitch_A-C,Tswitch_B-D ,Tswitch_A-D, Tswitch_B-C) = max(Tswitch_A-D, Tswitch_B-C)

## Slide 4
Case 1, UE granted with preferred Tx switching

## Slide 5
How it works for Case 1
Step 1: UE reports its preferred switching via “per-Tx-chain-based representation”for band combination (A,B,C,D)
Step 2: NW schedule a Tx switching as UEs preferred switching and sends the scheduled switching configuration to UE via “per-Tx-chain-based representation”
Step 3: UE performs the granted Tx switching, where the switching period is improved as:
    max(Tswitch_A-C,Tswitch_B-D)

## Slide 6
6
Case 2, UE granted with non-preferred Tx switching

## Slide 7
How it works for Case 2
Step 1: UE reports its preferred switching via “per-Tx-chain-based representation”for band combination (A,B,C,D)
Step 2: NW schedule a Tx switching as none UEs preferred switching and sends the scheduled switching configuration to UE via “per-Tx-chain-based representation”
Step 3: UE performs the granted Tx switching, where the default switching period applies:
    max {Tswitch_A-C,Tswitch_B-D, Tswitch_A-D, Tswitch_B-C}
    = max{Tswitch_A-D, Tswitch_B-C}