## Slide 1
On RRM Topics for Rel-19
3GPP TSG-RAN WG4 Meeting #110 R4-2401357
Athens, Greece, 26 Feb – 01 Mar, 2024
Agenda Item: 14
Document for: information
Huawei, HiSilicon

## Slide 2
EMR+ Fast SCell activation
RRM delay reduction
  FR2 unknown SCell activation based on Temporary RS
  L3 Measurement enhancement for FR1+FR2
Further RRM enhancement
  Interruptions at NR SRS antenna port switching
  L1/L2 mobility inter-frequency measurement enhancement
RRM evolution and enhancements

## Slide 3: EMR+ Fast SCell activation
Motivation
  Early measure in IDLE/Inactive mode is introduced in Rel-16 to setup CA upon UE entering connected mode. According to the existing known cell condition, the to-be-added SCell is regarded as “unknown” even if the EMR report is valid, then SCell activation procedure would follow unknown requirements when UE enters CONNECTED mode from IDLE mode.
  Fast SCell activation based on EMR is proposed to be enhanced when UE enters CONNECTED mode from IDLE/Inactive mode.
Objective
  Fast SCell activation with EMR reports upon UE enters connected mode
  Introduce corresponding signaling if needed.

## Slide 4: RRM delay reduction: FR2 unknown SCell activation based on Temporary RS
Motivation
  In Rel-18, one enhancement for FR2 SCell activation is to trigger L3 measurement by SCell activation command, and the activation delay can achieve comparable performance as known SCell activation. In Rel-17, Temporary RS is introduced for SCell activation delay reduction, which is not applicable for FR2 unknown cases without active serving in the same band.
  If Temporary RS can be utilized based on L3 measurement triggered by SCell activation command, the SCell activation delay can be further reduced.
Objective
  FR2 SCell activation delay further reduction base on Temporary RS and L3 measurement triggered by SCell activation command.
  Introduce corresponding signaling if needed.

## Slide 5: RRM delay reduction: L3 Measurement enhancement for FR1+FR2
Motivation
  Current status: Delay requirements for measurement outside gap are defined based on 2 searchers assumption for total CCs in FR1 and FR2
  Observation: In FR1+FR2 scenario, a UE supporting per-FR gap shall support totally 3 searchers to meet the requirements for measurement within gap in FR2 and outside gap in FR1
  Potential enhancement: when no gap is needed, the searcher within gap can be borrowed for outside gap, then 3 searchers are used for measurement outside gap. Shorter measurement delay for serving cell measurement (which is typically measured outside gap) can be achieved.
Objective
  Enhance CSSF (carrier-specific scaling factor) for L3 measurement outside gap in the above case
FR1 SCC
FR1 PCC
FR2 inter-freq with gap
X= 1
CSSF=1
CSSF=1
Measurement gap
CSSF= 2
CSSF= 2
CSSF=1
CSSF=1
CSSF=1
CSSF=1
Current requirements for within gap and outside gap
Current requirements for outside gap
Proposed solution for outside gap
FR1 SCC outside gap
FR1 PCC outside gap
FR2 SCC outside gap
PCC uses one searcher; all SCCs share the other searcher
PCC uses searcher#1; FR1 SCC uses searcher#2; FR2 SCC uses searcher#3;
Outside gap

## Slide 6: Further RRM enhancement: Interruptions at NR SRS antenna port switching
Motivation
  In current RRM spec, it is assumed that SRS resource for SRS antenna switching is allocated at the last 6 symbols of a slot. However, SRS starting in any symbol within a slot is already supported since Rel-16. Thus, some SRS antenna port switching scenarios are not covered by current RAN4 requirements.
  In Rel-17 interruption requirements at NR SRS antenna port switching, following scenarios are considered:
    Scenario 1: when X=1 SRS symbol is configured in a slot for SRS antenna port switching
    Scenario 2: otherwise, using X=6 SRS symbols in a slot as assumption of SRS transmission time
    Symbol level interruption requirement is only considered for scenario 1 for synchronized case. For all other cases, interruption requirement is defined in number of slots, which may be much longer than the actual interruption length.
Objective
  Interruption requirements at NR SRS antenna port switching when SRS starting in any symbol of a slot
  Finer granularity of interruption requirements at NR SRS antenna port switching (i.e. symbol level interruption length for more applicable scenarios)

## Slide 7: Further RRM enhancement: L1/L2 mobility inter-frequency measurement enhancement
Motivation
  According to current R18 LTM progress, only L1/L2 inter-frequency measurement with Type 1 gap is specified in R18.
  For UE who supports NCSG, during measurement occasion UE is expected to transmit and receive data on the corresponding serving carrier(s).
Objective
  L1/L2 inter-frequency measurement with NCSG (Network Controlled Small Gap)
    In FR1, SSB based L1-RSRP measurement can be performed simultaneously with L3-RSRP measurement;
    In FR2, SSB based L1-RSRP measurement is to be shared with L3 measurement with one NCSG, Or define a dedicated NCSG for L1-RSRP measurement