## Slide 1
Two Rel-19 WIs proposed for UE RF:
improved CA MPR for fragmented spectrum and SRS reporting for reciprocity-based DL-MIMO
Ericsson
Agenda item: 14
Document for: Information
3GPP TSG-RAN WG4 Meeting #110
Athens, Greece, 26 February – 1 March 2024
R4-2401854

## Slide 2: Improved MPR for non-contiguous intra-band CA
Improve coverage and TP in fragmented spectrum and combine with UL-MIMO or inter-band UL CA
Rel-19

## Slide 3: Background
For UL non-contigous intra-band CA configurations
  the MPR larger than that for the non-CA case for UL transmissions confined within one of the two carriers, e.g. the Pcell in the FDD example below, for UEs not indicating dualPA-Architecture
  the MPR for concurrent transmissions on two UL carriers very large, and only evaluated for Band n41
  hence significant reduction of UL coverage for CA in non-contigous spectrum
UL PCell
UL Scell
DL PCell
DL Scell
DL band
UL band
Common PA or a separate PA per CC/sub-block

## Slide 4: Objectives
Enhance performance of deployments in fragmented intra-band spectrum blocks
Improve coverage and TP for UL non-contiguous (NC) intra-band CA
  single UL cell scheduled/active: by reducing MPR to that of non-CA for UL transmissions confined within one of the two cells also for UEs not indicating dualPA-Architecture
    at least when one of the cells is deactivated but preferably when scheduled in one cell only
    for up to 100 MHz carrier separation (intraBandFreqSeparationUL-AggBW-GapBW-r16 class I) that can be supported by a single TX/PA and RX chain
  dual NC UL cells scheduled: by reducing MPR for concurrent transmissions for FDD and TDD regardless of PA architecture with additional side-conditions (LO leakage etc) if needed
  enhancements can be subject to UE capability
Introduce requirements for
  combinations of UL intra-band NC CA and UL-MIMO
  UL inter-band CA configurations with an UL intra-band NC part (without TX-switching)
Non-collocated intra-band NC cells can be considered

## Slide 5: Deployment scenarios (FDD examples)
By enhancing performance for single-PA architecture, a second TX/PA used for further improving the TP
  by UL non-contiguous intra-band CA + UL-MIMO in bands for which UL-MIMO is feasible or
  by an UL cell in another band in an UL inter-band CA configuration with an UL intra-band NC part and without TX switching
Two intra-band NC DL cells can always be configured
  the UL cell closer to the duplex gap deactivated if problems with UE receiver desense
  ’slow intra-band TX switching’ by switching the Pcell for load balancing, no intra-band TX switching: no UL gaps needed for TX switching and no DL interruptions: always non-CA MPR when single UL cell scheduled/activated
  3Tx not required
UL PCell
UL Scell
DL PCell
DL Scell
UL-MIMO + UL NC CA (dual PA)
MPR for non-CA when Scell not scheduled/activated
UL PCell
UL Scell
DL PCell
DL Scell
UL NC CA (single PA)
MPR for non-CA when Scell not scheduled/activated
UL Scell
DL SCell

## Slide 6
Enhancement of SRS performance and reporting
Improve reciprocity-based DL-MIMO performance
Rel-19

## Slide 7: Background
Poor SRS accuracy and variability degrade reciprocity-based DL-MIMO performance due to poor DL-CSI estimates
For SRS antenna switching, the actual SRS output power per SRS port(s) unknown
  Non-reciprocal insertion losses in the signal path(s) unknown
Received SRS power highly variable also under static conditions and can be significantly different between ports notwithstanding UE-antenna gain differences
SRS reporting schemes discussed for Rel-18 but no agreements in RAN4

## Slide 8: Objectives
Specification of a reporting scheme for SRS output power for all configured SRS resources of SRS resource sets (RAN4, RAN2)
  or non-reciprocal UE insertion loss per SRS port(s) if feasible
Limited changes to RAN1 specifications, no change of SRS power control or Type 3 PH
Improved testing of SRS output power
  essentially no testing of SRS in the UE conformance test specifications