## Slide 1
R4-2407589
Agenda Item: 13
Type: WID NEW
Document for: Information
3GPP TSG RAN WG4 Meeting #111
Fukuoka, Japan,
May 20th – 24th, 2024
Motivation for introduction of LTE FDD band in 1800 – 1830 MHz for Canada
Source: Novamint

## Slide 2
The 1800-1830 MHz spectrum has been exclusively designated at a national level for the use of electricity utilities in Canada.
The current regulation is based on WiMax characteristics, but the Canadian Regulator (ISED) is planning to update it to allow use of LTE
  The current regulation allows a maximum transmit power for the base station equal to 5W@5MHz and 10W@10MHz. Antenna gain is not considered in the above limits.
Pilots are ongoing or are planned to be conducted both in the lab and in the field later this year by several Electricity utilities.
Background

## Slide 3
Electricity utilities in the region have relied on WiMax operating in the 1800-1830 MHz range as the communication backbone only
Electricity utilities in Canada are eager to transition to LTE technology within the 1800-1830 MHz spectrum.
The telecom regulator in Canada, ISED, is already engaged in making the regulatory changes (like channel spacing) to make deploying LTE more optimal (moving from 125kHz to 100kHz channelization) on this band
This Work Item is proposing the definition of a new FDD band to transition from WiMax to LTE technology and allow new use cases, such LPWA (NB-IoT and eMTC)
Justification

## Slide 4
Proposals
Proposal 1 (Core)
Specify in a Release independent manner the characteristics of the new band:
  Band numbering and RF characteristics
  Channelization
  Duplex spacing
Define maximum transmit power for both eNB and UE in compliance with the current regulations (based on the adoption of WiMax)
Update the related 3GPP E-UTRA technical specifications to include support for the new band
Proposal 2 (Core)
Specify and modify core requirements (e.g. UE power class, Additional Maximum Power Reduction (A-MPR), Reference sensitivity, blocking performance) and specifications to support UE category M1&M2 and/or UE category NB1&NB2 in a release-independent way
Proposal 3 (Performance)
Update the related 3GPP E-UTRA technical specifications to include support for the new band, if necessary
Specify and modify performance requirements and specifications for the new LTE band to support UE category NB1&NB2 and category M1&M2 in a release-independent way

## Slide 5
Next Steps
The proposal aims to specify in a single step the new band and its application for NB1, NB2, Cat1M and Cat2M UEs
  Guidance is welcome from RAN4 if this is a feasible approach
Agree the WID on introduction of LTE FDD band in 1800 – 1830 MHz for Canada at RAN#104 (see R4-2407325)