## Slide 1: 3GPP TSG RAN4 Meeting #112 R4-2411509 Maastricht, Netherlands 19-23 August 2024 Agenda Item: 8.9.3 Source: Intelsat Title: Channel Bandwidth Mapping Document for: Discussion and Decision

## Slide 2: Introduction
The purpose of this contribution is to present the mapping of various Ku Band satellites’ bandwidths to established FR1-NTN and FR2 –NTN Numerologies.
The intention is to use 5G/NR technologies on Ku Band legacy and future satellite systems.
This contribution illustrates how Ku Band operational satellite transponders could be accommodated within FR1-NTN or FR2-NTN bandwidths. Furthermore, the spectrum wastage in each case is demonstrated.
The transponder data presented are operational Ku Band satellites services utilizing non-3GPP, proprietary technologies.

## Slide 3: Discussions
The data presented in following Table 1 represent the bandwidths of legacy and advanced Ku Band satellites in service.
Table 1 represents the bandwidths of legacy and advanced satellites systems that range from narrow 8 MHz to wide 662 MHz .
Table 1 illustrates how the legacy and advanced Ku Band transponders can be accommodated within FR1-NTN and FR2-NTN Numerologies. Furthermore Table 1 illustrates the wasted bandwidths in each case.

## Slide 4: Ku Band Satellite Transponder Bandwidths
Table 1 Legacy and advanced Ku Band Transponder Bandwidths mapped to FR1-NTN and FR2-NTN Numerologies
 | FR1 channel definition (MHz) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | FR2 channel definition (MHz) |  |  |  | 
Channel Bandwidth (MHz) | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100 | FR1 Wasted Bandwidth (MHz) | 50 | 100 | 200 | 400 | FR2 Unused Bandwidth (MHz)
8 |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 1 |  |  |  | 42
27 |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  | 3 | 1 |  |  |  | 23
36 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 4 | 1 |  |  |  | 14
54 |  |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  | 6 |  | 1 |  |  | 46
72 |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  | 8 |  | 1 |  |  | 28
108 |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 2 | 1 | 1 |  |  | 42
144 |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  | 1 | 1 | 1 | 1 |  |  | 6
216 |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  | 2 | 4 | 1 |  | 1 |  | 34
450 |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  | 4 | 0 | 1 |  |  | 1 | 0
662 |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  | 6 | 8 |  | 1 | 1 | 1 | 38

## Slide 5: Conclusions
The conclusions that we can draw from the presented analysis are as follows:
1- The FR1-NTN numerology can potentially accommodate the Ku Band legacy, advanced and future satellite transponder bandwidths with lower spectrum wastage.
2- The FR1-NTN Numerology allows for greater flexibility in deploying 5G/NR Services in the Ku Band provided we can address the outstanding issues in Appendix A
3- The FR2-NTN Numerology, can potentially has higher spectrum wastage compared to FR1-NTN.

## Slide 6: Appendix A: Discussions topics for RAN4
A few questions to RAN4
    1- Does the algorithm work on both uplink and downlink, or just downlink?
    2- What is the impact of algorithm on latency?
    3- How does the 5G device decide on how to construct multiple 5G channels given input satellite channel? What are the rules?
    4- What is the impact of the algorithm on processing and overhead?
    5- What are the maximum number of carriers that can be processed simultaneously ?
    6- Would a mix numerologies of FR1-NTN / FR2-NTN be considered?
Algorithm: the process of constructing and de-constructing of the multiple bandwidths see following Figures 1 and Figure 2

## Slide 7: Construct and Deconstruct(Illustrative Example1)
Figure1: Construct and De-construct of 500 MHz Bandwidth with multiple FR1 100 MHz Bandwidths

## Slide 8: Construct and Deconstruct(Illustrative Example2)
Figure2: 220 MHz FR1 Bandwidth for 216 MHz Transponder