## Slide 1: Tx switching for 3Tx UEs
MediaTek Inc., China Telecom, China Unicom, OPPO, Softbank, T-Mobile USA, Verizon
3GPP TSG-RAN WG4 Meeting # 112 R4-2411783
Maastricht, Netherlands, 19th – 23th Aug, 2024 Agenda Item 11

## Slide 2: Introduction
In Rel-18,
  One first step toward 3Tx was introduced via the following the non-spectrum WI 4Rx_low_NR_band_handheld_3Tx_NR_CA_ENDC and the spectrum WI R18_3Tx_NR_CA_ENDC. Allowing 3Tx chains on top of PC2 and PC1.5 framework provides configuration flexibility for UL-MIMO when UE is operating with UL CA, leading to further UL throughput improvement.
In Rel-19,
  It is important to consider the evolution path to further utilize the 3Tx architecture to achieve even better performance. In the newly approved Rel-19 WI NR_ENDC_RF_Ph4, one objective for HPUE with CA was introduced to discuss the general requirements for 3Tx UE.
  On spectrum-related Wis, according to the approved RP-240894, the 3Tx requirements will be distribtued into multiple baskets, such as PC3: DC_R19_xBLTE_yBNR/NR_CADC_SUL_R19 for PC3 and HPUE_DC_LTE_NR_R19/HPUE_NR_CADC_SUL_R19 for HPUE.
  In above WIs, FDD 2Tx + TDD 1Tx for 3Tx UEs is one of the main differences to Rel-18 WIs, which only involve FDD 1Tx + TDD 2Tx

## Slide 3: Discussions
Since both FDD 1Tx + TDD 2Tx and FDD 2Tx + TDD 1Tx are ready in the 3GPP spec, we can further consider a Tx switching between above 2 scenarios.
  With Dynamic Tx switching, network can fully utilize UE antennas to further improve the UL throughput. E.g., by default, 2Tx in TDD to enjoy the larger BW, and switch to 2Tx in FDD when UE moves to cell edge or during the TDD DL slots.
On spec impact, almost all existing requirements, signaling and capabilities can be directly reused, such as switching period, dualUL, interruption, ... etc. The details can left to RAN4.
Proposal: Consider introducing Tx switching between FDD 1Tx + TDD 2Tx and FDD 2Tx + TDD 1Tx in Rel-19 RAN4 package in Dec’24.
U
U
U
U
FDD
D
D
D
S
TDD
U
U
U
U
D
D
D
D
U
U
U
U
FDD
D
D
D
S
TDD CC#1
U
U
U
U
D
D
D
D
D
D
D
S
TDD CC#2
U
U
U
U
2Tx
1Tx
switch period
Maximize UL Tput by using FDD MIMO
Maximize UL Tput by using TDD MIMO& larger BW

## Slide 4: Summary
  Proposal 1: Consider introducing Tx switching between FDD 1Tx + TDD 2Tx and FDD 2Tx + TDD 1Tx in Rel-19 RAN4 package in Dec’24.

## Slide 5: Thank you!