## Slide 1: NR A-MPR reevaluation scenarios on n1 for Japan
KDDI, NTT Docomo
3GPP TSG-RAN WG4 Meeting #112-bis R4-2415439
Hefei, Anhui, China, 14th - 18th, October 2024
Agenda : 4.4.1
Document for: Discussion

## Slide 2: 1. Introduction
In Japan, a discussion is ongoing about MOP relaxation. In Rel-15, based on operators’ requirements [1], NS_05 for n1 has been supported to protect domestic PHS (Personal Handy-phone System), and it will be shut down in near future.
This means that the current NS_05 for n1 can be relaxed, but also there is still a necessary for protecting the other domestic digital cordless-phone service instead of PHS.
Relevant to the possible relaxation for PC3, this paper is intended to propose necessary evaluation to specify new NS_05 for n1.

## Slide 3: 2. Discussion
Current additional spurious emission requirements on NS_05/NS_05U [1] is as follows:
Table 6.5.3.3.4-1: Additional requirements for "NS_05" and “NS_05U”
On the other hand, the domestic protection requirement will be modified as follows:
  BW = 5MHz for PC3
    1884.5-1910.0 MHz : -30 dBm/MHz
    1910.0-1915.7 MHz : -25 dBm/MHz
  BW = 10/15/20MHz for PC3
    1884.5-1906.6 MHz : -30 dBm/MHz
    1906.6-1915.7 MHz : -25 dBm/MHz
Frequency range (MHz) | Channel bandwidth (MHz) / Spectrum emission limit (dBm) | Measurement bandwidth | 
 | 5, 10, 15, 20 |  | 
1884.5 £ f £ 1915.7 | -41 | 300 kHz | 

## Slide 4: 2. Discussion
Up to 20MHz CBW of n1 has been supported since Rel-15 with current NS_05 and NS_05U (all the sections/Tables are in TS 38-101-1 sec 6.2.3.4) for protecting PHS.
So far, the max output power is limited according to TS 38.101-1 Table 6.2.3.4-1, 6.2.3.4-2, 6.2.3.4-3 and 6.2.3.4-10.
On the other hand, due to the MOP relaxation discussion for PC3, increasing MOP will be allowed soon in Japan. Then we’d like to prepare for the updated as:
Proposal 1: Invite reevaluation/simulation results for modified NS_05/NS_05U for PC3 for RAN4#113 Nov.

## Slide 5: Band n1 – in 1920-1940 MHz cases
Can smaller A-MPR values be expected than those of current NS_05/NS_05U for Case#1-#8 ?
1920
1925
1930
1935
1940
15MHz
20MHz
10MHz
15MHz
No A-MPR?
1922.5≦fc＜1924.2
1930.0≦fc＜1945.7
Range of Fc
1927.5≦fc＜1932.5
1932.5≦fc＜1938.2
1925.0≦fc＜1930.0
1930.7 ≦fc＜1945.0
10MHz
1930.0≦fc＜1930.7
10MHz
1924.2
(5MHz/SEM)
1924.2≦fc＜1927.5
5MHz
5MHz
f
(MHz)
No A-MPR?
1930.7
(10MHz/SEM)
1938.2
(15MHz/SEM)
1945.7
(20MHz/SEM)
Case#1:
Case#2:
Case#3:
Case#4:
Case#5:
Case#6:
Case#7:
Case#8:

## Slide 6: Band n1 – in 1940-1960 MHz case
General spurious emission
Digital cordless-phone service protection
SEM
1940
1950
1960
f(MHz)
1920
1915.7
1906.6
-25dBm/MHz
-30dBm/MHz
20MHz
-25dBm/MHz
-30dBm/MHz
  In current spec, A-MPR is defined for only 20 MHz CBW (Fc = 1950 MHz), no A-MPR for less than 20MHz CBW.
  With regulatory update, no A-MPR is needed even for 20MHz CBW for Digital cordless-phone service protection as it can be met by SEM and general spurious emission.
    Note: NS_05U requires the same A-MPR with NS_100 to meet UTRA ACLR

## Slide 7: 2. Discussion
As usual, we prefer to support modified NS_05/NS_05U from the earliest possible release, but also it is up to marketing or implementation plans of UE/chipset vendors. We’d like to collect the views on preferred release.
To leave some flexibility for the release, if situation permits, we’d like to conduct this activity under a maintenance AI. (it is up to RAN4 Chair’s decision.)
Proposal 2: If situation permits, we’d like to conduct this activity under a maintenance AI for the flexibility of the first release applied.

## Slide 8: 3. Conclusion
Proposal 1: Invite reevaluation/simulation results for modified NS_05/NS_05U for RAN4#113 Nov.
Proposal 2: If situation permits, we’d like to conduct this activity under a maintenance AI for the flexibility of the first release applied.
R4-1803744 NR A-MPR evaluation scenarios for n1 and n8 for Japan, RAN4#86bis
4. Reference

## Slide 9: EOF