## Slide 1
Motivation on simplification of CA band combination
3GPP TSG-RAN WG4 Meeting #112bis R4-2415638
Hefei, China, October 14 - 18, 2024
Agenda Item: 9
Document for: Discussion
Huawei, HiSilicon

## Slide 2
Motivation
  3GPP RAN4 defines the band combinations with the number of carriers consisting of all available spectrum of one operator, up to 6 CCs for NR band combination and up to 8 CCs for EN-DC configuration currently, such as CA_n1-n3-n7-n28-n38-n78 as defined in Table 5.2A.2.5-1 of TS 38.101-1 and DC_1A-3A-5A-7A-7A_n40A-n77(2A) as defined in Table 5.5B.4.5-1 of TS 38.101-3.
  The larger number of carriers for the band combinations results in very high RF complexity, complicated UE capability and high implementation cost, all these will lead to long development cycle and delay the delivery of service to customer.
  With the introduction of larger channel bandwidth for medium-band, massive MIMO is more mature to use, most UEs can support 4Rx for the spectrum above 1.7GHz which greatly improves the spectral efficiency.
  The data rate for some typical applications, such as VOIP video call, WeChat, short/long video, navigation, live broadcast, games, file download, conference and etc., can be well met by using NR larger channel, massive MIMO and limited number of aggregated carriers.
  The user experienced data rate requested by ITU-2030 is >100-500 Mbit/s, the main challenge is the throughput that can be achieved at the cell edge.
  With certain spectrum combination and flexible scheduling schemes, such as sub1GHz, 1.5~3GHz and 3~7GHz, the max peak throughput of DL 1.6Gbps and UL 600Mbps can be achieved, this will efficiently reduce the number of CA combinations:
Simplification on CA band combination
Frequency Range | Channel Bandwidth per CC | MIMO layer# | Max throughout | Target Scenario
sub1GHz | ≥10MHz | DL：2 UL：1 | DL：100Mbps UL：60Mbps | Larger coverage，basic communication service
1.5~3GHz | ≥20MHz | DL：4 UL：2 | DL：400Mbps UL：200Mbps | General traffic coverage
3~7GHz | ≥70MHz | DL：4 UL：2 | DL：1.12Gbps UL：350Mbps | Heavy-traffic service；estimated TDD pattern is 7:3
≥10GHz | ≥100MHz | DL/UL：2 | DL：500Mbps UL：125Mbps | Hotspot enhancement；estimated TDD pattern is 8:2

## Slide 3
Complex RF front-end: complex multiplexing solutions coupled with SRS transmission
  The parallel transmission and reception of many bands will bring high design cost of combiner;
  Front-end loss will result in max output power and sensitivity decrease;
  SRS switching will lead to front-end control logic coupling and interruption;
  More than 1dB front-end insertion loss can be observed for UE with complicated CA compared to single band.
Benefit of simplification of RF front-end
  Simplified multiplexer will bring 0.7~1dB insertion loss decrease, >5% cost reduction and about 300mW PA power reduction (10% profit @max Pout that will benefits the scenarios with Uplink Full Power)
  The SRS interruption probability decreases, and the NR-CA/EN-DC data rate increases.
Simplification of CA band combination – RF front-end

## Slide 4
Transceiver scale continues to increase
  The number of TX/RX channels of UE transceivers increases continuously, the TX/RX channels are coupled with different MIMO numbers additionally, which leads to a high proportion of specification redundancy and implementation costs
  For example:
Simplification of CA band combination – Transceiver
Frequency range | <1GHz | 1~3GHz | 3~7GHz
Case: DC_1A-3A-5A-7A-7A_n40A-n77(2A) | B5: 2RX | B1/3/7(7A_7A): 4RX n40: 4RX | n77(77A_77A): 4RX
Path# | Max: 30 RX paths, 8 PLL; Note 1: In real application, it is seldom to activate so many carriers at the same time. |  | 
Principle | Each RX in each CC in inter-band CA or non-contiguous CA, currently a separate RX path is needed; Each CC in inter-band CA or non-contiguous CA, currently one dedicated PLL is needed. |  | 
Benefit of simplification of transceiver
  Transceiver RX specifications can be reduced 50%+ compared with the maximum specifications of 30 RX chains, if only 14 RX chains are maintained.
  The complexity of UE TX switching among different band combinations can be greatly.

## Slide 5
High product engineering delivery cost
  Extremely complex UE capabilities
  Huge number of CA combination test
  Large scale calibration of production line
Simplification of CA band combination – UE Capability
Number of BC
Benefit of UE capability simplification
  Reduced UE capability size
    UE capability storage can be reduced by 50%+ for 3 bands CA
  Reduced testing scale
    Multi-carrier specifications can be reduced by ~45%
    Avoid complex test rule design, such as selection of MSD combination and TX in which band.
  Simplified product line calibration scale
    According to the scalable rule, calibration can be reduced by 45%+

## Slide 6
Current frequency range definition characteristic
  Most bands with FDD duplex mode are defined within sub1GHz and 1.4~2.2GHz
  Narrow spectrum bandwidth for single operator
  High cost for CA in the same frequency range
Proposal 1:
  Define five frequency ranges for FR1: sub1GHz, 1.4~2.2GHz, 2.3~2.7GHz, 3.3~5GHz, 5~7GHz
  Introduce inter-band CA with max five bands for the target user experienced rate
  Select one band within each of the FR1 five frequency ranges for CA band combination
Simplification of CA band combinations – Frequency range
Sub 1GHz
1.4~2.2GHz
2.3~2.7GHz
3.3~5GHz
5~7GHz
FR3
FR2
No. of bands
CC1
CC2
CC3
CC4
CC5
CC6
CC7
21
22
8
4
5
CC6
7
NR
LTE
25
27
6
4
2
NA
NA
Duplex mode
FDD
FDD
TDD
TDD
TDD
TDD
TDD
Target Scenario
CC#
Wide coverage，basic data rate and voice
Wide coverage, data rate enhancement
Higher data rate
Higher data rate
Wide coverage, data rate enhancement
directional reinforcement
Hotspot

## Slide 7
Max number of RX chain for CA+MIMO capability:
  For the suggested five frequency ranges definition, we can assume that UE supports the following number of RX chain, but the total number of RX chain X+Y+Z+W+V as UE capability:
Simplification of CA band combinations – Max RX chain
Proposal 2: Define UE capability of the supported max number of RX chain for CA+MIMO
Frequency Range | RX chain# | UE supported RX chain#
sub1GHz | 2Rx | X
1.4~2.2GHz | 2Rx/4Rx, CPE with TDD max 8RX | Y
2.3~2.7GHz | 2Rx/4Rx, CPE with TDD max 8Rx | Z
3.3~5GHz | 2Rx/4Rx, CPE with TDD max 8Rx | W
5~7GHz | 2Rx/4Rx, CPE with TDD max 8Rx | V
  For example: to meet a certain target data rate, UE has capability to support max 14 RX chains. UE can flexibly support the following reconfigurable CA+MIMO scenarios:
    ① 2(sub1GHz)+4(1.4~2.7GHz)+8(3.3~5GHz)；
    ② 2(sub1GHz)+4(1.4~2.7GHz)+4(3.3~5GHz)+4(5~7GHz).