## Slide 1: MediaTek Views on RAN4 Rel-20 5G-A
MediaTek Inc.
3GPP TSG-RAN WG4 Meeting # 114 R4-2501625
Athens, Greece, Feb 17-21, 2025 Agenda Item 10

## Slide 2: Outline
General views for Rel-20 RAN4-led 5G-A WIs
MTK proposals to Individual Areas: RF, RRM and Demod

## Slide 3: General views for Rel-20 RAN4-led 5G-A WIs
Many new features were added without following commercialization. It is not an efficient way of using the time and efforts of all RAN4 delegates.
New Rel-20 features needs to focus on
  Addressing operator’s urgent deployment problem and need
  Balanced focus in eMBB and vertical markets
  Simple and efficient solution to increase the deploying chance

## Slide 4: MediaTek Proposals to Individual Areas
Area | Proposed objectives
UE RF | DL Fragmented Carriers
 | Tx switching for 3Tx UEs
 | NTN CA
Area | Proposed objectives
RRM | HO interruption minimization
 | Interruption-Free DCI Reception
 | Relaxed RLM/BFD measurement for Redcap
Area | Proposed objectives
Demod | App layer throughput enh: OLLA and 4-layer
 | CQI report for R-ML SU-MIMO receiver
 | Test case for new special channel model

## Slide 5: RF - DL Fragmented Carriers - Tx switching for 3Tx UEs - NTN CA

## Slide 6: DL Fragmented Carriers
Motivations
  DL fragmented carriers containing more than one non-contiguous CC in the same band consuming multiple Rx RF chains. It may limit the maximum supported number of CCs due to the limited number of the Rx RF chains as well as the baseband processor capabilities in the UEs. This limitation prevents operators from fully utilizing their fragmented spectrum holdings. Documents were submitted to RAN#102 [RP-233374] and RAN4#110 [R4-2402309] indicating this global problem and potential solution.
  The SI [RP-243002] was approved in Rel-19 to investigate solutions with the focus of single DL band with 2CC NCCA within frequency span ≤ 100 MHz, under the assumption of inter-operator co-located scenario.
    Impacted requirements such as ΔRIBNC, ACS and in-band blocking
    Potential new mechanism for a UE to inform network on the need to enable semi-statical switching of UE hardware resources
  Following the outcome of the SI, it is important to start the nominal work item phase in Rel-20 to really resolve the concern of global operators on fragmented carrier.
Objectives (core part)
  This work aims at introducing the mechanism and UE requirements to enable DL fragmented carrier with the following assumptions:
    Single DL band with 2CC co-located NCCA within frequency span ≤ 100 MHz
    Up to 6 dB DL received PSD imbalance between the two non-contiguous CCs
    Semi-statically switch hardware resources
  Under co-located inter-operator scenario
    Specify new ΔRIBNC requirements for one Rx RF chain mode and new ACS and in-band blocking requirements with the interference power level from co-located adjacent channel operators based on SI outcome [RAN4] ;
      TBD other identified requirements during SI.
    Specify new measurement and report mechanism to enable semi-statically switch of hardware resources, based on SI outcome [RAN4, RAN2]
      Discuss UE measurement behavior and specify corresponding RRM requirement [RAN4]
      Introduce required RRC signaling and UE capability, based on RAN4 conclusions [RAN2]
  Under non-co-located inter-operator scenario
    Identify which RF requirements could be adjusted and the need of updating the mechanism (introduced for co-located inter-operator scenario) for hardware resource switch
    Depending on the study conclusions, specify the identified requirements and the updated mechanism
Objectives (Perf part)
  If agreed, specify the measurement accuracy requirement
  If agreed, specify the RRM test cases
  on-collocated inter-operator
  RRM part: measure report  UE switching delay …
  RAN2: measure, report, UE capability,

## Slide 7: Tx switching for 3Tx UEs
Motivation
  Starting from Rel-18, 3Tx UE has been introduced in non-spectrum and spectrum WIs.
  Rel-19 continues the further enhancement with HPUE with CA for 3Tx UE objectives in non-spectrum WI NR_ENDC_RF_Ph4 and spectrum Wis (DC_R19_xBLTE_yBNR, NR_CADC_SUL_R19, HPUE_DC_LTE_NR_R19, HPUE_NR_CADC_SUL_R19).
  Following the evaluation path of further enhancing 3Tx, further Tx switching should be considered.
    With Dynamic Tx switching, network can fully utilize the UE Tx capability to maximize the UL throughput, e.g.
      TDD 2Tx + FDD 1Tx during the TDD UL slots when the UE experiences good channel conditions
      TDD 1Tx + FDD 2TX when TDD channel conditions is worse, or during the TDD DL slots
Objectives
  Specify dynamic UL Tx switching between FDD 1Tx + TDD 2Tx and FDD 2Tx + TDD 1Tx:
    Extend existing physical layer UL Tx switching framework to support the new switching cases [RAN1]
    Specify RF and RRM requirements to enable the new switching cases [RAN4]
    Specify configuration and UE capability RRC signaling for the feature [RAN2]
U
U
U
U
FDD
D
D
D
S
TDD
U
U
U
U
D
D
D
D
2Tx
1Tx
Worse TDD conditions or DL slots
Good TDD conditions

## Slide 8: Carrier Aggregation for NTN
Motivation
  NTN has been introduced since Rel-17, but till Rel-19 the scope is limited to single carrier. To further improve the system throughput, carrier aggregation (CA) is a very efficient approach and should be considered as the next step.
  For example, according to RP-243301, some satellite operators have the Ku band transponder bandwidth such as 72MHz and 250MHz, which required intra-band contiguous CA for better utilization
Proposal
  This work aims at introducing CA for NTN with the following assumptions:
    Intra-satellite scenarios
    Both handheld & non-handheld devices
  DL CA (1st priority)
    Specify the band combo and requirements for introduce intra-band CCA, intra-band NCCA and inter-band CA.
      Note: the fragmented carrier for NTN NCCA should not start before the TN WI has reached stable conclusions.
  UL CA (2nd priority)
    Specify the band combo and requirements for inter-band CA with PC3 per-band and intra-band CCA
    Study the UE architecture for Intra-band NCCA. If agreed, introduce the corresponding band combos and requirements

## Slide 9: RRM - Handover Interruption Minimization - Interruption-Free DCI Reception - Relaxed RLM/BFD Measurement for Redcap

## Slide 10: Handover Interruption Minimization
Motivations
  Early DL synchronization before handover
    In Rel-18 LTM, new mechanism were introduced for network to request UE to start early DL synchronization toward a target cell. It can reduce the later cell switch time by skipping the time waiting for SSB for DL synchronization.
      This mechanism is triggered by TCI state activation, which requires additional signal overhead.
    In fact, this early DL synchronization behavior can be autonomously done by UE. In other words, the benefit of faster handover delay can also be achieved in legacy handover.
  Postponed interruption (in case time for synchronization during handover is still needed)
    In current spec, UE stops source cell data Tx/Rx after receiving HO command. However, during HO delay, most of the time were spent waiting for SSB of the target cell. This waiting time can be better leveraged to reduce interruption.
Objectives
  Early DL synchronization before handover
    Introduce an enhanced UE behavior to start autonomous early pre-synchronization to neighboring cells
      Study and identify the applicable conditions
    Under the applicable conditions, define the reduced handover delay without additional time for synchronization
  Postponed interruption (in case time for synchronization during handover is still needed)
    Introduce an enhanced HO delay requirement by leveraging the waiting time of SSB to reduce interruption.
    Phase 1: Start from Rel-15 HO requirements.
    Phase 2: FFS whether and how to extend to conditional HO, HO with PSCell and LTM cell switch.
    If needed, LS can be sent to RAN2 to trigger RRC signalling change, based on RAN4 consensus
SSB
RACH
Proc time
waiting time
HO cmd
SSB
RACH
Proc 1
HO cmd
Proc 2
Legacy interruption time
Reduced interruption time
Enhancement!

## Slide 11: Interruption-Free DCI Reception
Motivations
  In current 38.133, there is a long list of interruption requirements. One very common reason for these interruptions is due to UE’s RF re-tuning.
    The current assumption of RF re-tuning time are 0.5ms in FR1 and 0.25ms in FR2. These RF re-tuning time will likely interrupt the whole slot
  The interruption requirements are defined based on the missing ACK/NACK from UE to network.
    It is commonly understood that interrupting DCI would cause more serious issue in network scheduling. Compared to interrupting PDSCH. PDCCH requires better protections because it may carry more important indications, such as UL grant, BWP switch, TCI-state switch.
  One the other hand, some features, e.g., UL Tx switching, SRS carrier switching, already require a shorter RF re-tuning time. Therefore, it is possible to investigate how to explore this shorter RF re-tuning time to protect PDCCH for performance improvement.
Objectives
  Introduce UEs capable of interruption-free DCI reception with reduced RF re-tuning time.
  Identify which existing interruption requirements can be enhanced with the enhanced UE behavior.
  If needed, introduce new requirements or modify existing requirements for UEs capable of interruption-free DCI reception
PDCCH
PDSCH
PDCCH
PDSCH
Interruption
Interruption

## Slide 12: Relaxed RLM/BFD Measurement for Redcap
Motivations
  All power saving features are very important to Redcap UEs.
  Unfortunately, the feature of relaxed RLM/BFD measurement and Redcap were not considered jointly in Rel-17 due to concurrent discussions.
  For 2Rx Redcap UEs, the requirements for relaxed RLM/BFD measurement can directly follow existing requirements for non-Redcap UE.
  For 1Rx Redcap UEs, some discussions are needed to decide the scaling factor in the relaxed measurements
Objectives
  Extend Rel-17 RLM/BFD measurement relaxation requirements to Redcap UEs

## Slide 13: Demodulation - Application layer throughput enh: OLLA and 4-layer - CQI report for R-ML SU-MIMO receiver - Test case for new special channel model

## Slide 14: Demodulation
Motivations
  Application layer throughput enh: OLLA and 4-layer
    Leftover of Rel-18 Demod work. Extending the current scope to consider OLLA and 4-layer provides an even better assessment of UE performance in the real deployment scenario.
      At least UE performance should not be degraded when OLLA is enabled
  CQI report for R-ML SU-MIMO receiver
    Advanced R-ML SU-MIMO receiver is already considered in current PDSCH demodulation test, but not in the CQI test. This mismatch needs to be fixed. So that we do need to wait for OLLA to converge
  Test case for new spatial channel model
    SI FS_NR_demod_SCM is expected to introduce new channel model which explores the spatial characteristic of the channel. As the next step, it is expected to define the corresponding test cases.
Objectives
  App layer throughput enh: OLLA and 4-layer
    Specify absolute physical layer throughput requirements with link adaptation with
      Outer-loop link adaptation at gNB side enabled, and/or
      4-layer MIMO
  CQI report for R-ML receiver
    Introduce the CQI test cases for advanced R-ML receivers
  Test case for new spatial channel model
    Introduce Throughput and PMI test cases with the channel model based on the outcome of SI for SU-MIMO with single cell and with neighboring cell interference

## Slide 15: Thank you!