## Slide 1: Views on Rel-20 RAN4-led topics
Source: ZTE, Sanechips
Agenda: 10
3GPP TSG WG RAN4#114
Athens, Greece, Feb 17-21, 2025
R4-2501882

## Slide 2
Content
01
BS RF related enhancement
UE RF related enhancement
02
UE RRM related enhancement
03
Demod related enhancement
04

## Slide 3: Repeater for NTN deployment
In Rel-17, RF repeater is introduced to improve the coverage of terrestrial network.
In Rel-18, NCR is introduced to further improve its performance on top of RF repeater
In Rel-19, lots of HPUE related enhancement is approved to further improve the UL coverage.
From our understanding, the coverage issue for NTN scenario should be worse than the terrestrial network, then how to improve the coverage from network deployment perspective is also critical. Rel-17 RF repeater could be well leveraged for coverage enhancement for NTN scenario.
In Rel-20, we propose to specify the RF repeater for NTN scenario.

## Slide 4: Co-location requirement for BS RF requirement
Co-location requirement is still under the discussion in Rel-19. MCL 30dBc is leveraged from FR1 low bands which might be not applicable for FR1 high bands e.g. U6GHz.
Due to the high workload for Rel-19 BS RF enhancement, we propose to have the formal discussion on co-location requirement in Rel-20.
Antenna type | 2.6G-BS1 | 2.6G-BS2 | 3.5G-BS1 | 3.5G-BS2 | 4.9G-BS1
Isolation in vertical domain(dB) | <-54 | <-57 | <-52 | <-53 | <-56
Isolation in horizontal domain | <-31 | <-40 | <-34 | <-35 | <-46

## Slide 5: LP-WUS in the TN MSR specification
LP-WUS related BS RF requirement is still under the discussion in Rel-19, however it only focus on single RAT BS RF requirement. Considering the LP-WUS feature could be also potentially in the FR1 low bands especially from LP-WUS coverage perspective.
For FR1 low bands, lots of BS are implmented as MSR BS instead of single RAT BS, in other words, to specify the LP-WUS related requirement for NR RAT only is not sufficient.
In Rel-20, we propose to specify the LP-WUS related requirement in MSR specification which is similar as NB-IoT operation in NR in-band in Rel-16.

## Slide 6: Others proposals for BS RF enhancement in Rel-20
Multi-band repeater or NCR in FR2 similar as Rel-18 FR2 multi-band operation;
Multi-band (e)IAB in FR2 similar as Rel-18 FR2 multi-band operation;
MSR SAN specification to include both standalone NB-IoT over NTN, eMTC over NTN, SAN NTN and also NB-IoT operation in NR in-band for SAN.

## Slide 7
Content
01
BS RF related enhancement
UE RF related enhancement
02
UE RRM related enhancement
03
Demod related enhancement
04

## Slide 8: Rx switching in FDD band combination in Rel-20
Low-low band Rx switching has been agreed to be introdouced in Rel-19, however due to the limited TU, it mainly focus on FDD band+SDL band combination only.
For low-low FDD band combinations, due to the supported frequency range for FR1 low bands (e.g. less than 1GHz) limited to be around 100MHz without considering antenna retuning, lots of frequency spanning range of band combination is wide than 100MHz (e.g. band n5+n8)
In Rel-20, we propose to specify Low-low band switching between FDD band combinations.

## Slide 9: Coherent UL MIMO in FDD band combination in Rel-20
Coherent UL MIMO has been introduced from Rel-15 specification, however we failed to see the commercial product on the market due to the potential following limitations.
  RF chains between RFIC are well synchronized (e.g. shared PLL and share Qgen circuit)
  Additional timing misalignment caused by PA, front-end filter/combiner etc.
In Rel-20, we propose to study how to make the UL-MIMO to be commercially available e.g. introducing certain mechanism by leveraging the current DPD feedlink.

## Slide 10: Other proposals for UE RF enhancement in Rel-20
HPUE IoT NTN TDD
  Motivation: PC3 IoT NTN TDD is expected to be completed in Rel-19. To further enhance the UL converage, HPUE IoT NTN TDD can be a potential enhancenment in Rel-20.
PC2 NTN Redcap
  Motivation: PC3 NTN RedCap is expected to be completed in Rel-19. PC2 FDD TN RedCap is also discussing in Rel-19, PC2 NTN Redcap can be a potential enhancenment in Rel-20.
Fragment carrier
  Motivation: R19 SID -> R20 WID. (Scope can be further discussed)
Band combination simplification
  Motivation: HPUE MSD rule is expected to be completed in Rel-19 which make it possble to further simply the HPUE band combiantion in Rel-20.

## Slide 11
Content
01
BS RF related enhancement
UE RF related enhancement
02
UE RRM related enhancement
03
Demod related enhancement
04

## Slide 12: NTN-TN handover in Rel-20
NTN-TN handover is one important feature to improve the user experience. Currently only cell re-selection requirement between NTN and TN was defined, however RRM requirement for NTN-TN handover requirement is still missing.
In Rel-20, we propose to define the RRM requirement for NTN-TN handover.

## Slide 13: Scell with uplink only transmission in Rel-20
Scell with uplink only transmission has been discussed in the previous release, lots of merits and applicable use case as listed in following have been identified and well discussed. However due to the workload and limited TU restrictions, RRM requirement for Scell with uplink only transmission has not been specified yet until Rel-19. In order to enable this feature with full set of requirements in RAN4, it’s proposed to define the corresponding RRM requirement for it in Rel-20.
In Rel-20, we propose to specify the RRM requirement for it:
  To define the RRM requirement for Scell with UL only transmission [RAN4].
  Potential RAN1/2 impact if any could be triggered by LS.

## Slide 14
Content
01
BS RF related enhancement
UE RF related enhancement
02
UE RRM related enhancement
03
Demod related enhancement
04

## Slide 15: UE Demod related evolution in Rel-20
In Rel-15, single carrier demod requirements with MMSE/MMSE-IRC and R-ML receiver for scenario of single-user with multiple layer transmission were defined. In Rel-17, the single carrier demod requirements for MMSE-IRC receiver for intra-cell inter-user interference under MU-MIMO scenario and inter-cell interference scenario are agreed to be defined. For Rel-18, the single carrier performance requirements for intra-cell inter -user interference under MU-MIMO scenario with R-ML receiver was defined.
Compared to IS and ML receivers, IC type of receivers are also non-linear. However, whiling maintaining an accept level of complexity complexity, they can improve performance to a certain extent.

## Slide 16: BS Demod related evolution in Rel-20
In Rel-19, the BS demodulation single carrier performance requirements for UL co-channel interference with MMSE-IRC receiver was defined. In practical network deployment, DL to UL interference becomes an increasingly significant scenario that cannot be ignored.

## Slide 17: Thanks