## Slide 1: WF on 200 MHz channel bandwidth
3GPP TSG-RAN WG4 Meeting #114bis
Wuhan, Hubei, China, 07th – 11th April, 2025
R4-2503718
KDDI, China Unicom, China Telecom, BT, Bouygues Telecom, Deutsche Telekom, KPN, Vodafone, Orange, Odido, Telefonica, Telenor, TIM, Telia Company, Spark NZ, Jio Platforms(JPL), Telstra, NTT Docomo, SoftBank, CKH IOD UK LTD, Ericsson, Huawei

## Slide 2: Background
China has identified the band 6425-7125 MHz for IMT, this came into effect 1st July 2023, see Chinese table of allocations and has given certainty that the band will be for 5G/6G, here.
UAE has added the band 6425-7125 MHz to their IMT holdings expects actual operation to begin between the years 2025 and 2026 by 2025/2026, here.
RCC Recommendation 1/21 to harmonize the technical conditions for 6425-7125 MHz, including channel used by 5G/IMT-2020 systems can consist of one or more adjacent frequency blocks but should not exceed 400 MHz.
The Indian Government decided to allocate the entire Upper 6 GHz band for IMT (3GPP n104), with different parts of the band being made available through to 2030, Cabinet Approves Spectrum Refarming for 5G and Future 6G Services: Report
Brazil's National Telecommunications Agency (Anatel) identified the upper 6 GHz for IMT in Jan, 2025 and has now announced a draft schedule for frequency auctions over the next decade (2026–2036) , including 6 GHz in 2026, SEI/ANATEL - 13277590 - Draft Resolution
The amount of spectrum for each operator in these markets is expected to be at least 200 MHz.
200 MHz of spectrum per operator is also expected to be relevant for other markets.
Certainty needs to be given to operators and regulators that 200 MHz channel bandwidth will be supported by 3GPP.
Notes: In the 5G era, the non-collocated scenarios for B42 and n77/n78 as shown in the previous slides still occur in Japanese, Korean and European operators. Tx antenna co-location at network side is not always available since the co-existence conditions are not always same for all the bands.

## Slide 3: Study technical areas
Sub-carrier spacing for 200MHz CBW
  30kHz recommended
Transmission bandwidth configuration and guard bands
Correct scaling of emissions mask
FRC bandwidth
  50MHz FRC could be defined for RX testing, since 20MHz FRC may lead to excessive test time
Impacts to RAN1/2 specification
  RAN1 limit on number of PRBs
(In case 60kHz SCS would be selected, RAN4 demodulation requirements etc. needed)
Notes: In the 5G era, the non-collocated scenarios for B42 and n77/n78 as shown in the previous slides still occur in Japanese, Korean and European operators. Tx antenna co-location at network side is not always available since the co-existence conditions are not always same for all the bands.

## Slide 4: Way forward
200 MHz channel bandwidth will be developed by 3GPP in Rel-20 considering n104.
Notes: In the 5G era, the non-collocated scenarios for B42 and n77/n78 as shown in the previous slides still occur in Japanese, Korean and European operators. Tx antenna co-location at network side is not always available since the co-existence conditions are not always same for all the bands.

## Slide 5
EOF