## Slide 1: Way Forward on 4Rx PDSCH, 3 and 4 Layers and SDR, performance
Ericsson,
3GPP TSG-RAN WG4 Meeting #76bis R4-156875
Sophia Antipolis, France, 12th – 16th Oct 2015

## Slide 2: Agreements in 4Rx Adhoc
Main session agreements for 3 and 4 layers PDSCH tests
  Proposal 5 : The demodulation tests with 3-MIMO layer and 4-MIMO layers are conducted in 4-RX bands where the UE indicates up to 4-MIMO layer supports through the UE capability report of supportedMIMO-CapabilityDL.
Propose the test scenarios with 3 and 4 layers for PDSCH based on the agreements made as following
  Test 1: 3layer, TM3, 4x4 low, EVA70
  Test 2: 4 layer, TM4,4x4 low, EPA5, followed wideband PMI
    To ensure the feasible SNR test point
  Test 3: 4 layer, TM9,4x4 low, EPA5, followed wideband PMI
    To ensure the feasible SNR test point

## Slide 3: Current Proposals & Observations for 3 and 4 Layers
Qualcomm
  TM3 rank 3 test with MCS 18
  TM4 rank 4 test with MCS 14
  TM9 rank 3 test with MCS 18
Huawei
  Test 1: 3layer, TM3, MCS14, 4x4 low, EVA70
  Test 2: 4 layer, TM4, MCS14, 4x4 low, EPA5, followed wideband PMI
  Test 3: 4 layer, TM9, MCS14, 4x4 low, EPA5, followed wideband PMI
ZTE
  TM4, 3 layers, 4x4 XP new medium, MCS14
  TM9, 4 layers, 4x4 low, MCS14
  TM9, 3 layers, 4x4 low, 256QAM MCS20, CFI =1
MTK:
  1) TM3, 3 layers
  2) TM4, 4 layers
  3) TM9, 3 layers
LG:
  Observations 1. Using 2 CCH need additional loss up to 1 dB for layer 3 and 1.5 dB for layer 4 compared to 1 CCH.
  Observations 2. Using XP medium need additional loss up to 1.5 dB for layer 3 and 2 dB for layer 4 compared to ULA Low.
  Observations 3. if we consider 3 % EVM and impairment margin, all test case seems feasible at least MCS14 with 64 QAM case.
  Observations 4. For Layer 3 with 256QAM, all simulated TMs seem feasible.
  Observations 5. For Layer 4 with 256QAM, all simulated TMs seem infeasible because of its too much high geometry.

## Slide 4: To be studied 3&4 Layers
Test 1: 3layer, TM3, 4x4 low, EVA70
Test 2: 4 layer, TM4,4x4 low, EPA5, followed wideband PMI
  To ensure the feasible SNR test point
Test 3: 4 layer, TM9,4x4 low, EPA5, followed wideband PMI
  To ensure the feasible SNR test point

## Slide 5: Current Proposals & Observations for SDR testing
Qualcomm:
  Proposal 2. For SDR test, select TM3 with rank 4 PDSCH as transmission mode.
  Proposal 3. Specify SDR test for both 64QAM and 256QAM.
  Proposal 4. Select MCS 27 for 64QAM rank 4 SDR test. For 256QAM rank 4 SDR test, consider MCS 26 in case Tx EVM requirement can be tightened to 3%. Otherwise, consider MCS 25.
  Proposal 5. Consider following SDR test applicability rule for rank 4 UE.
  Apply rank 2 SDR test to a CA configuration and bandwidth combination with largest aggregated bandwidth.
  Apply rank 4 SDR test to a CA configuration and bandwidth combination supporting 4 layer with largest aggregated bandwidth.
Huawei:
  Proposal 2: It’s confirmed that the proposed SDR test setups are feasible for PDSCH 4 layer:
  64QAM with reasonable highest coding rate
  6% EVM
  TM3, 4x4 static channel
  Proposal 3: Further study is needed in RAN4 to clarify the 4 layer SDR tests, at least for
  256QAM based 4 layer SDR test
  Applicable UE category for 4 layer SDR test
ZTE:
  Proposal4: TM3 should be used for 4Rx SDR tests.
  Proposal5: Use MCS27 for 64QAM and MCS21 for 256QAM for 4 layers SDR test.
Mediatek
  Proposal 4: Consider 256QAM with 4 layer in SDR test.
  Proposal 5: Remain using TM3 in SDR test.
LG:
  Observation 6. For 64QAM, MCS28 seems feasible regardless of any TB success rate.
  Observation 7. For 256QAM, MCS26 seems feasible regardless of any TB success rate.

## Slide 6: To be studied on SDR tests
TM3
  MCS27 4 Layers for 64QAM
  MCS TBD 4 Layers for 256QAM
  CA tests to be considered