## Slide 1: NB-IOT standalone operation: Co-existence study
Nokia Networks
R4-157925
3GPP TSG-RAN WG4 #77
Anaheim, CA, US, 16 – 20 Nov, 2015
Agenda Item: 7.50.3
Document for information

## Slide 2: References
GERAN TR 45.820
TR 36.942
TR 25.942
[1] RP-151621, “New Work Item: NarrowBand IOT (NB-IOT)”, Qualcomm
[2] R4-156755, “Way Forward on Simulation Assumptions and Methodology for NB-IOT coexistence study”, Nokia Networks, Ericsson, ZTE

## Slide 3: NB-IOT standalone operation: background
NB-IOT is operating within 200kHz

## Slide 4: NB-IOT standalone operation: co-existence study with GSM
Co-existence study shall be used to evaluate interference of NB-IOT with deployment.
Static system level simulation, as used for RAN4 co-existence study, shall be used to evaluate interference impact.
Cases for standalone operation
  15kHz subcarrier spacing NB-IOT, coexistence with GSM
  15kHz subcarrier spacing NB-IOT, coexistence with GSM with a 100kHz separation.

## Slide 5: Assumption of GSM Frequency planning
Channel bandwidth is 200 kHz and occupied bandwidth is 180 kHz for NB-IOT.
For the GSM system, frequency reuse is according to one of the following:
  4/12 – 12 frequencies used over a cluster of 4 sites (12 sectors)
Single cell reuse is applied for NB-IOT
A1
A2
A3
B1
B2
B3
C1
C2
C3
D1
D2
D3
A1
A2
A3
B1
B2
B3
C1
C2
C3
D1
D2
D3
A1
A2
A3
B1
B2
B3
C1
C2
C3
D1
D2
D3
A1
A2
A3
B1
B2
B3
C1
C2
C3
D1
D2
D3

## Slide 6: Evaluation methodology
The co-existence study methodology follows TR 36.942 in general.
Static system simulation
NB-IOTGSM interference
  Adjacent 200kHz channel interference
GSM  NB-IOT interference
  Adjacent 200kHz channel interference
Metrics:
  SINR distributions and degraded SINR distributions due to ACI are shown for both NB-IOT and GSM.

## Slide 7: Simulation Assumptions
Parameter | Value | 
Frequncy | 900MHz | 
GSM system | 4/12 – 12 frequencies used over a cluster of 4 sites (12 sectors) | 
Network layout | Wrap around 57 sectors (figure 4.3 in TR 36.942); NB-IOT and GSM BS are not co-collocated. | 
BS Tx power | 43dBm/200kHz | 
Separation between NB-IOT and GSM carriers | 0Hz, 100kHz | 
UE max transmit power | 23dBm | 
NB-IOT UE max transmit power | 23dBm | 
ACS | 33dB | 
DL power control | N/A | 
UL power control | based on sub-clause 5.1.1.6 of 3GPP TR 36.942 | 
UE antenna gain | 0dBi | 
Penetration loss | Based on Annex D.1 of TR 45.820 (No additional building penetration loss for the NB-IoT as aggressor) | 

## Slide 8: NB-IOT filtering
Filtering is applied for NB-IOT base station.
  Assume that the Tx filtering for NB-IOT can meet the GSM spectrum mask.
GSM spectrum mask

## Slide 9: NB-IOT  GSM, with 0Hz separation
Simulation results show SINR distribution and degraded SINR due to ACI, for all cells and NB-IOT neighbor cells.
Average ACI over all GSM UE is limited; however, there is significant ACI for the neighbor GSM carrier.

## Slide 10: NB-IOT  GSM: with 100kHz separation
Simulation results show SINR distribution and degraded SINR due to ACI, for all cells and NB-IOT neighbor cells.
The ACI to GSM is limited due to the 100kHz separation.

## Slide 11: GSM  NB-IOT: with 0Hz separation
In general, GSM impact to NB-IOT is mainly from the GSM carrier that is close to the NB-IOT frequency.

## Slide 12: GSM  NB-IOT, with 100kHz separation
With 100kHz separation, the impact to NB-IOT is insignificant.

## Slide 13: Observations
DL co-existence simulation results are provided for NB-IOT coexistence with GSM.
For NB-IOT  GSM (victim),
  With 0Hz separation, average ACI over all GSM UE is limited; however, there is significant ACI for the neighbor GSM carrier.
  With 100kHz separation, the NB-IOT impact to GSM is very small.
For GSM NB-IOT (victim),
  With 0Hz separation, GSM impact to NB-IOT is mainly from the GSM carrier that is close to the NB-IOT frequency.
  With 100kHz separation, the impact to NB-IOT is insignificant.