## Slide 1: NB-IOT guard band operation: Co-existence study
Nokia Networks
R4-157927
3GPP TSG-RAN WG4 #77
Anaheim, CA, US, 16 – 20 Nov, 2015
Agenda Item: 7.50.3
Document for information

## Slide 2: References
GERAN TR 45.820
TR 36.942
TR 25.942
[1] RP-151621, “New Work Item: NarrowBand IOT (NB-IOT)”, Qualcomm
[2] R4-156755, “Way Forward on Simulation Assumptions and Methodology for NB-IOT coexistence study”, Nokia Networks, Ericsson, ZTE

## Slide 3: NB-IOT guard band operation: background
Guard band operation
  NB-IOT is operating at one PRB with 0Hz or 200kHz separation from LTE PRBs
  One PRB is used for NB-IOT
Two DL approaches
  15kHz subcarrier spacing
  3.75kHz subcarrier spacing

## Slide 4: NB-IOT guard band operation: co-existence study
Co-existence study shall be used to evaluate mutual interference between LTE and NB-IOT for guard band operation.
Static system level simulation, as used for RAN4 co-existence study, shall be used to evaluate interference impact.
Cases for guard band operation
  15kHz subcarrier spacing, with 0Hz separation: no need for co-existence study
  3.75kHz subcarrier spacing, with 0Hz separation
  3.75kHz subcarrier spacing, with 200kHz separation
This contribution provides simulation results for DL co-existence study.

## Slide 5: Evaluation methodology
The co-existence study methodology follows TR 36.942, and simulation assumption contribution R4-156755
Static system simulation
  ACLR is reused at PRB level.
NB-IOTLTE interference
  Adjacent PRB interference, specified with ACLR at PRB level.
LTE  NB-IOT interference
  Adjacent PRB interference, specified with ACLR at PRB level.
Other relevant parameters to follow RAN1 agreements captured in R1- 156264
Metrics:
  For NB-IOT use SINR
  For LTE use SINR and throughput loss (based on SINR to throughput mapping in 36.942)

## Slide 6: Simulation Assumptions
Parameter | Value | 
Frequncy | 2GHz | 
LTE system bandwidth | 10 MHz | 
Network layout | Wrap around 57 sectors (figure 4.2 in TR 36.942) | 
Base station total TX power | 46 dBm, shared by all LTE PRBs and NB-IoT | 
NB-IOT Power boosting | 6dB | 
Separation between NB-IOT and LTE carriers | 0Hz, 200kHz | 
UE max transmit power | 23dBm | 
NB-IOT UE max transmit power | 23dBm | 
ACS | LTE: 33dB; NB-IOT: 35dB | 
DL power control | N/A | 
UL power control | based on sub-clause 5.1.1.6 of 3GPP TR 36.942 | 
UE antenna gain | 0dBi | 
Penetration loss | Based on Annex D.1 of TR 45.820 (No additional building penetration loss for the NB-IoT as aggressor) | 

## Slide 7: Interference model
NB-IOTLTE (victim) interference
  The adjacent PRB interference is evaluated with ACLR at 180kHz (1PRB) offset (with 0Hz separation), and 400kHz offset (with 200kHz separation)
LTE  NB-IOT (victim)
  Adjacent PRB interference is evaluated with ACLR.

## Slide 8: Performance evaluation
Performance evaluation shall be based on TR 36.942 and [2]. The degradation of SINR and LTE throughput shall be presented as a function of ACIR
  ACIR is evaluated based on

## Slide 9: ACLR and Typical ACIR values
ACLR shall be based on single PRB to evaluate NB-IOT impact
  ACLR = Mean power of 1 PRB / mean power of neighbor PRB
NB-IOT (3.75kHz)  LTE (victim)
  Use GSM Tx SEM: ACLR1 = 29dB.
  Use LTE ACS=33dB.  ACIR = 27.5dB
LTE  NB-IOT (victim)
  Typical LTE ACLR (45dB) is base on full LTE bandwidth (1.4MHz and beyond) (36.104).
  There is no specified LTE ACLR and LTE SEM at single PRB level.
   It is not clear about the typical ACIR value.

## Slide 10: NB-IOT (3.75kHz spacing)  LTE
NB-IOT interference to LTE is very small given a large LTE BW (50PRB).
Typical ACIR=27.5dB
Typical ACIR=27.5dB

## Slide 11: NB-IOT LTE at the edge PRB
NB-IOT at guard band operation has little impact to average LTE UE
However, for the edge PRB close to the NB-IOT’s PRB, the average SINR loss is significant, depending on ACIR value.
Typical ACIR=27.5dB

## Slide 12: LTE  NB-IOT (3.75kHz spacing)
SINR degradation due to adjacent LTE interference
    The average SINR degradation will be in the range of 0~1dB, depending on ACIR values.

## Slide 13: Observations
There is no need to study the guard band operation of NB-IOT with 15kHz subcarrier spacing design for DL co-existence.
DL co-existence simulation results are provided for NB-IOT guard band operation with 3.75kHz subcarrier design
For NB-IOT  LTE (victim),
  LTE throughput loss is small for 10MHz LTE system;
  However, the edge PRB (close to the NB-IOT) will suffer ~0.5dB SINR loss in average.
For LTE NB-IOT (victim),
  The average SINR degradation will be in the range of 0~1dB, depending on ACIR values.