## Slide 1: WF on BS demod performance for new PUCCH formats
Nokia Networks, Alcatel Lucent, Ericsson, NTT Docomo, Huawei
R4-161221
3GPP TSG-RAN WG4 Meeting #78
St. Julian’s, Malta, 15 - 19 February 2016
Agenda Item: 6.14.1

## Slide 2: Proposals
BS demod performance requirements for PUCCH format 4 are defined in Rel-13.
  It is open whether to define performance requirements for PUCCH format 5 in Rel-13
  Companies are encouraged to provide performance comparison between PF4 and PF5 in RAN4#78bis
BS demod performance requirements are defined as the SNR levels to achieve
  Option 1: 99% CRC pass rate in presence of signal, or
  Option 2: 1% BLER in presence of signal, or
  Option 3: 1% missed ACK rate.
The requirements apply regardless whether the message contents include HARQ-ACK, or P-CSI, or both.
Following payload sizes are used for the simulation evaluations.
  24bits
  48bits
  128bits
  Other assumptions for the performance tests are in the next slide.
  Interested companies are encouraged to conduct simulations based on agreed assumptions and provide results for calibration in RAN4#78bis.

## Slide 3: Other simulation assumptions
Codeword selection | Random selection for both HARQ-ACK and P-CSI
Codebooks | [Semi-static (codebooksizeDetermination-r13=1)]
ACK repetitions | Disabled
Propagation conditions | EPA5, EVA70 Propagation channel definitions to be reused from 36.104.
Cyclic Prefix | Normal CP
Channel BWs | 10, 15, 20MHz
Carrier definition | Carrier frequency: 2.0 GHz PUCCH on PCell (single PUCCH group) Number of PRBs for PF 4: FFS
PUCCH multiplexing | 1 UE
Antenna’s configuration | UE: 1Tx BS: 2Rx, 4Rx, 8Rx correlation between branches is 0 no power imbalance between branches
Timing estimation | Perfect timing estimation
Frequency hopping | At slot boundary
Power control | Off