## Slide 1: WF on sub-6GHz ACLR and ACS
Nokia, Alcatel-Lucent Shanghai Bell
3GPP TSG-RAN WG4 Meeting #83 Hangzhou, China, 15 - 19 May, 2017
Agenda Item: 10.3.5
R4-1706062

## Slide 2: Background
Contributions on sub-6GHz NR BS and UE ACLR and ACS have been discussed in RAN4#83:
  [1] R4-1705743 Discussion on co-existence study for NR uplink NTT DOCOMO, INC.
  [2] R4-1705671 Sub6 ACS Qualcomm Incorporated
  [3] R4-1705657 UE sub-6 GHz ACS considerations and proposals Intel Corporation
  [4] R4-1705702 Conducted UE ACLR for frequency range 1 Nokia, Alcatel-Lucent Shanghai Bell, Qualcomm Incorporated
  [5] R4-1705429 Proposal on below 6GHz NR BS ACLR and ACS Nokia, Alcatel-Lucent Shanghai Bell
  [6] R4-1704929 Co-existence performance for NR_NR co-existence on sub-6GHz CATT

## Slide 3: Way forward on BS (conducted) ACLR
Adopt the E-UTRA BS (45dB) ACLR1 and ACLR2 to all NR BS classes for wanted channel bandwidth up to 20MHz.
  ACLR for other NR wanted channel bandwidth are FFS.
  The adjacent channel has the same channel bandwidth as the transmitted carrier.
  For bands defined also for UTRA, the adjacent channel bandwidth is the corresponding UTRA (FDD or TDD) channel bandwidth.
  E-UTRA adjacent channel bandwidth other than 5MHz are FFS.
Adopt each E-UTRA BS absolute limit to the corresponding NR BS class , whichever is less stringent compared to the ACLR.

## Slide 4: Way forward on BS (conducted) ACS
Adopt the E-UTRA BS (46dB) ACS to all NR BS classes
  The allowed REFSEN degradation is 6dB.
  The adjacent channel bandwidth is FFS.

## Slide 5: Way forward on UE (conducted) ACLR
NR-Sub6ACLR1 = 30dB for power class 3 for wanted channel bandwidth up to 20MHz.
  Other power class is FFS.
  The adjacent channel bandwidth the same as the wanted signal.
  NR-Sub6ACLR1 for other NR wanted channel bandwidth are FFS.
  E-UTRAACLR1 for different channel bandwidth is FFS.
For bands defined also for UTRA, adopt UTRAACLR1 = 33dB and UTRAACLR2 =36dB for power class 3.
Adopt the E-UTRA UE (-50dBm) absolute limit, whichever is less stringent compared to the ACLR1 or ACLR2.

## Slide 6: Way forward on UE (conducted) ACS
ACS = 33dB for wanted channel bandwidth up to 20MHz.
  ACS for other NR wanted channel bandwidth are FFS.
  The adjacent channel bandwidth the same as the wanted signal.
  ACS for different adjacent channel bandwidth are FFS.
  ACS may be updated as SNR for Refsens is currently TBD.
Case 1: Refsens+14dB for wanted signal and Refsens+45.5 dB for interferer.
Case 2: -56.5dBm for wanted signal and -25dBm for interferer.
  Case 1 and 2 is based on IM=2.5dB and SNR=-1dB.