## Slide 1: WF on single Tx switched UL
R4-1711551

## Slide 2: Tentative agreements from Ad-Hoc
Topic 1: Which IM is categorized difficult?
  Proposals made during Ad-hoc:
    IM2
    IM2 and IM3
      IM2 always and IM3 without restrictions
      IM2 always and IM3 with restrictions
        Only IM3 with L-L (below 1GHz) or H-H (1.695-2.695GHz) combinations is difficult
    MSD level
    IM2 to IM4
    IM2 to IM5
Tentative agreement: choose B and reference architecture shall be further studied and limiting impact to PCell shall be studied

## Slide 3: Tentative agreements from Ad-Hoc
Topic 2: Is the categorization based on band combinations or channel assignments?
General understanding: Channel allocations without IM2 or IM3 are considered as easy despite the band combination has channel allocations with IM2 or IM3 impact.
Tentative agreement: Use formula to define which channels are affected. Put the formula example to the WF.

## Slide 4: WF proposal
Inter-band combinations that have IM2 are categorized difficult and inter-band combinations that have IM3 for L-L and H-H combinations are categorized difficult.
Formula’s are used to define which channel combinations within difficult inter-band combinations are not affected by IM2 and 3
  Concurrent 2 UL is mandatory for these channel combinations
RAN4 shall study the impact of different RF architectures, and decide what to do based on the outcome. If there is a difference it shall be accounted
RAN4 shall study if and how to account the TX power level in categorization process
The treatment of secondary component carriers (no UL active within that band)
  A) The IMD impact to LTE secondary component carriers shall not be considered
  B) The IMD impact to LTE secondary component carriers shall be agreed in ran4#85 meeting including looking into different IMD order treatment
For intra-band contiguous DC_71_n71 with 20 MHz maximum aggregated bandwidth, simultaneous 2 UL transmission is mandatory

## Slide 5: WF proposal
Formula:
  Interference bandwidth: IBW = |a| x CBW1 + |b| x CBW2
    |a| + |b| = 2 (or 3)
    CBW1 and CBW2 are UL channels
  Center frequency of IBW: fIBW = a x f1 + b x f2
    f1 and f2 are center frequency of each UL channel
  The range of IMD 2 (or 3): [fIBW – IBW/2, fIBW + IBW/2]
RAN4 shall discuss the definition of UL and DL channels in the next meeting
  Alt.1. spectrum holdings of a operator in a band
  Alt.2. aggregated UE channel bandwidth configured by the network
  Alt.3. transmission bandwidth

## Slide 6: WF proposal
Send LS to RAN2 to inform RAN4 agreements
LS to RAN2:
  RAN4 informs RAN2 that categorization shall be per band combination. In addition, RAN4 shall inform that all easy channel combinations within difficult band combinations shall support concurrent 2UL

## Slide 7: Appendix 1: Example Band Combinations including IMD2 and 3 issues
IMD2 or IMD3 may hit Rx channel of PCell based on the location of UL channels
LTE Band (FDD) | NR Band (TDD) | IMD Order Falling in Rx Band
1 | n77 | 2
3 | n77 | 2
3 | n78 | 2
18 | n77 | 2
28 | n50 | 2
20 | n28 | 3

## Slide 8: Appendix 2: Example how to evaluate easy/difficult channel assignments
There is IM2 relation for at least one BW combination within an inter-band combination => IM2 hits own RX channel => Difficult IM2
Operator A has the following frequencies within difficult band combination defined above
  BX UL 1800-1810, BX DL 1850-1860
  nY UL/DL (TDD) 3640-3660
  => IM2_low =3640-1810=1830, IM2_high=3660-1800=1860
  => channel combination specific IM2 hits own RX channel =>Difficult IM2=> 2UL not mandatory for this channel combination
Operator B has the following frequencies within difficult band combination defined above
  BX UL 1810-1820, BX DL 1860-1870
  nY UL/DL (TDD) 3640-3660
  => IM2_low =3640-1820=1820, IM2_high=3660-1810=1850
  => channel combination specific IM2 doesn’t hit own RX channel =>Easy IM2=>2UL mandatory for this channel combination