## Slide 1: NR A-MPR evaluation scenarios for n1 and n8 for Japan
SoftBank, KDDI, NTTdocomo
3GPP TSG-RAN WG4 Meeting #86bis R4-1803744
Melbourne, Australia, 16 - 20 April, 2018
Agenda : 7.1.2.1.2
Document for: approval

## Slide 2: A-MPR simulations for n1
n1: two types of evaluation needed as per current NS_05
  NS_05 Note 1(>= 1915.7+ 4 +CBW)
    Note 1 was modified through the study of Band 65, mainly to exempt A-MPR for 10/15MHz above 1940MHz
    We hope to confirm whether Note 1 above is applicable for NR as well.
    If not applicable, several cases such as shown in Slide-4 need to be checked.
  NS_05 Note 2(1920-1940MHz)
    In addition to Note 2, several cases for NR as shown in Slide-5 need to be checked.
  For 1920-1940MHz region, we expect that CBWs not indicated in slide-5 will be subject to Note 1: up to 1dB Backoff when RB is more than or equal to 50. If Note 1 is not applicable for this region, additional case(s) may be requested by one operator.

## Slide 3: A-MPR simulations for n8
n8: as per R4-1702772(approved in Apr. 17) – replacement of current RB restriction
  The following scenarios are sufficient :
    5MHz @ 900-905MHz,
    10MHz @ 905-915MHz and
    15MHz @ 900-915MHz

## Slide 4: Band n1 – in 1940-1960MHz cases
  For 20 MHz CBW (Fc = 1950 MHz)
    To check required A-MPR for both Inner and Outer (A-MPR <= 1 dB for >= 50RB has been used in LTE)
  For 10 and 15 MHz CBW (Fc = 1945 and 1947.5 MHz)
    To check if “For 10MHz channel bandwidth whose carrier frequency is larger than or equal to 1945 MHz or 15 MHz channel bandwidth whose carrier frequency is larger than or equal to 1947.5 MHz, no A-MPR applies.” in NOTE 1 in TS 36.101 Table 6.2.4-1 can be maintained in NR as well
    If not, required A-MPR values for both Inner and Outer
1940
1945
1950
1955
1960
15MHz
20MHz
Case#1:
Case#2:
Case#3
10MHz
No A-MPR?
How much
A-MPR?
1947.5

## Slide 5: Band n1 – in 1920-1940MHz cases
For Case#1 and #2, TS36.101 has specified these cases. Can smaller A-MPR values be expected for NR than those of LTE?
For Case#3 - #6, new cases are shown. We would like to know how much A-MPR values are needed to protect PHS. For Case#5 and #6, FeMTC evaluation results would be useful.
1920
1925
1930
1935
1940
15MHz
20MHz
Case#1:
Case#2:
Case#3:
Case#4:
Case#5:
Case#6:
10MHz
5MHz
LTE spec exists
LTE spec exists
New for NR
New for NR
New for NR
New for NR
15MHz
5MHz
Hope to confirm no A-MPR is necessary.
How much
A-MPR?