## Slide 1: The principle of defining measurement requirements without gap sharing
NTT DOCOMO, INC.
R4-1804608
Document for: Approval
3GPP TSG-RAN WG4 86bis
Melbourne, Australia, 16 - 20 April 2018
Agenda item: 7.9.3.4

## Slide 2: Background
The introduction of gap sharing feature was agreed last year, which is the same principle as LTE eMTC.
Regarding LTE eMTC case,
  IE for gap sharing is needed to indicate the ratio of measurement period between intra-frequency and inter-frequency measurements due to the following reasons.
  MGRP is the only way to indicate each measurement timing and duration for eMTC UE.
  Only one type of MGRP can be configured among intra-frequency and inter-frequency measurements.
Regarding NR case,
  SMTC can indicate the measurement period for intra-frequency and inter-frequency measurements since SMTC can be configured for each carrier frequency.
  Regarding RLM, the ratio of SSBs to be used between RLM and intra/inter-frequency measurements can be indicated by configured SSB periodicity, SMTC periodicity and MGRP.
  IE for NR gap sharing is not included in Rel.15 TS 38.331 now.

## Slide 3: Proposals
For FR2 PCell/PSCell, RLM requirements for the case that SMTC periodicity equals to TSSB are not specified, and RLM requirements is defined by assuming that intra-frequency measurement is performed at the SSB timing covered by SMTC window.
  For FR1, it would not necessary to consider collision between RLM-RS and SMTC window to determine evaluation periods for RLM.
  See R4-1804613 for detail.
Regarding SSB-based measurements, the delay requirements can be scaled by SMTC periodicity and the number of carriers instead of gap sharing IE.
  We will show the detail of this factor from next slides with some examples.

## Slide 4: The principle of scaling factor
Premise conditions
  All of SMTC periodicities for inter-frequency measurements are not larger than the length of MGRP.
  In case that SMTC periodicity and offset are the same, the same delay requirements can be applied.
  SSBs to be measured are allocated from the carriers which have the longest SMTC periodicity of all.
  The carriers configured by shorter SMTC periodicity have higher priority than the carriers configured by longer SMTC periodicity in terms of the number of SSBs to be measured.
Proposed scaling factor and parameters:
* If multiple carriers ( ) are configured by SMTC_X and offset, for each carriers is scaled by .
Parameter | Detail
SMTC_X | The SMTC periodicity to be calculated
SMTC_Y | the longer SMTC periodicity than SMTC_X periodicity
 | the maximum SMTC periodicity among all of measured carriers
 | the number of carriers which SMTC is overlapped with the largest SMTC periodicity except for the carriers configured by the largest SMTC periodicity
 | the number of carriers which SMTC (<SMTC_Y) is overlapped with SMTC_Y except for the carriers configured by SMTC_Y
 | the number of carriers which SMTC (<SMTC_X) is overlapped with SMTC_X except for the carriers configured by SMTC_X
 | the scaling factor for SMTC_Y
Parameter | Detail
SMTC_X | The SMTC periodicity to be calculated
SMTC_Y | the longer SMTC periodicity than SMTC_X periodicity
 | the maximum SMTC periodicity among all of measured carriers
 | the number of carriers which SMTC is overlapped with the largest SMTC periodicity except for the carriers configured by the largest SMTC periodicity
 | the number of carriers which SMTC (<SMTC_Y) is overlapped with SMTC_Y except for the carriers configured by SMTC_Y
 | the number of carriers which SMTC (<SMTC_X) is overlapped with SMTC_X except for the carriers configured by SMTC_X
 | the scaling factor for SMTC_Y

## Slide 5: Example 1
Conditions
  SMTC periodicity for intra-frequency measurement and inter-frequency measurement are the same (SMTC_A).
    intra-frequency measurements w/gap includes following cases:
      SSBs to be measured outside BWP.
      BWP covers SSBs to be measured, but it is overlapped with measurement gap.
  MGRP is the same value as SMTC_A periodicity.
  All of SMTC windows are overlapped with measurement gap.
TSSB
SMTC_A periodicity
Intra-freq
(SMTC_A)
Inter-freq
(SMTC_A)
MG
SSB
SMTC_B periodicity
MG
MG
SSBs to be used for measurement
SSBs not to be used for measurement
TSSB | 10ms
SMTC_A | 40ms
MGRP | 40ms
Scaling factor for each carrier
Example of parameter
If example of parameters are used, can be calculated as follows:
(No longer SMTC carriers than SMTC_A)

## Slide 6: Example 2
Conditions
  SMTC periodicity for intra-frequency measurement and inter-frequency measurement are the same (SMTC_A), but either one has SMTC offset, which value is SMTC_A periodicity/2.
    intra-frequency measurements w/gap includes following cases:
      SSBs to be measured outside BWP
      BWP covers SSBs to be measured, but it is overlapped with measurement gap.
  All of SMTC windows are overlapped with measurement gap.
TSSB
SMTC_A periodicity
Intra-freq
(SMTC_A)
Inter-freq
(SMTC_A)
MG
SSB
SMTC_A periodicity
MG
MG
TSSB | 10ms | Offset
SMTC_A | 80ms | 0ms
SMTC_A | 80ms | 40ms
MGRP | 40ms | -
SSBs to be used for measurement
SSBs not to be used for measurement
MG
Offset
Scaling factor for each carrier
Example of parameter
If example of parameters are used, can be calculated as follows:
(No longer SMTC carriers than SMTC_A)

## Slide 7: Example 3(1)
Conditions
  SMTC periodicity for intra-frequency measurement and inter-frequency measurement are different.
    intra-frequency measurements w/gap includes following cases:
      SSB outside BWP
  MGRP is the same value as min(SMTC_A, SMTC_B).
  All of SMTC windows are overlapped with measurement gap.
TSSB | 10ms
SMTC_A | 20ms
SMTC_B | 40ms
MGRP | 20ms
TSSB
SMTC_A periodicity
MG
SSB
SMTC_B periodicity
Intra-freq
(SMTC_A)
Inter-freq
(SMTC_B)
Scaling factor for SMTC_B
SSBs to be used for measurement
SSBs not to be used for measurement
1. Regarding scaling factor for SMTC_B carrier, can be calculated as follows:
Example of parameter
If example of parameters are used,
(No longer SMTC carriers than SMTC_B)

## Slide 8: Example 3(2)
Scaling factor for SMTC_A
2. Regarding scaling factor for SMTC_A carrier, can be calculated as follows:
The number of SSBs used by SMTC_B carrier
(the number of carriers which SMTC (<SMTC_B) is overlapped with SMTC_B except for the carriers configured by SMTC_B)

## Slide 9: Example 4(1)
Conditions
  SMTC periodicity for intra-frequency measurement and inter-frequency measurement are different.
    intra-frequency measurements w/gap includes following cases:
      BWP covers SSB, but it is overlapped with measurement gap.
  MGRP is the smaller value than max(SMTC_A, SMTC_B, SMTC_C).
  SMTC windows are overlapped with measurement gap partially.
TSSB
SMTC_A periodicity
MG
SSB
SMTC_B periodicity
SMTC_C periodicity
Intra-freq
(SMTC_A)
Inter-freq
(SMTC_B)
Inter-freq
(SMTC_C)
SSBs to be used for measurement
SSBs not to be used for measurement
TSSB | 10ms
SMTC_A | 20ms
SMTC_B | 40ms
SMTC_C | 80ms
MGRP | 40ms
Example of parameter

## Slide 10: Example 4(2)
Scaling factor for SMTC_B
2. Regarding scaling factor for SMTC_B carrier, can be calculated as follows:
Scaling factor for SMTC_C
1. Regarding scaling factor for SMTC_C carrier, can be calculated as follows:
SSBs used by SMTC_C carrier
If example of parameters are used,
(No longer SMTC carriers than SMTC_C)
(the number of carriers which SMTC (<SMTC_A) is overlapped with SMTC_A except for the carriers configured by SMTC_A)
(the number of carriers configured by SMTC_C)

## Slide 11: Example 4(3)
Scaling factor for SMTC_A
3. Regarding scaling factor for SMTC_A carrier, can be calculated as follows:
SSBs used by SMTC_C carrier
SSBs used by SMTC_B carrier
(the number of carriers configured by SMTC_C)
(the number of carriers configured by SMTC_B)