## Slide 1: Way forward on SSB-based intra-frequency measurement requirements
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 7.9.4.1
R4-1804749

## Slide 2: Background
There is good chance that the measurement gaps configured for inter-frequency measurement partially or fully overlap with the SMTC configured for the intra-frequency measurement as illustrated in Fig.

## Slide 3: Way forward
For SSB-based intra-frequency measurement without gap
  is introduced to address the overlap issue between gap and SMTC when considering the SSB-based intra-frequency measurement period requirements.
    The performance of intra-frequency measurement without gap as specified in section 9.2.5 when SMTC configured for intra-frequency measurement are partially overlapping with measurement gaps, is scaled by M = MGRP / (MGRP – SMTCperiod)

## Slide 4: Way forward
For SSB-based intra-frequency measurement with gaps
  Reuse Kintra to scale the intra-frequency measurement requirements when UE requires measurement gaps to identify and measure intra-frequency cells or when SMTC configured for intra-frequency measurement are fully overlapping with measurement gaps and when UE is configured to identify and measure cells on inter-frequency carriers
    The performance of intra-frequency measurement with gap as specified in section 9.2.6 is scaled by Kintra = 1/X * 100
    The performance of intra-frequency measurement without gap as specified in section 9.2.5 when SMTC configured for intra-frequency measurement are fully overlapping with measurement gaps, is scaled by Kintra = 1/X * 100
    The performance of inter-frequency measurement as specified in section 9.3 is scaled by Kinter = 1/(100-X) * 100