## Slide 1: WF on NR PRACH demodulation requriements
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#86bis
Melbourne, Australia, April 16th – 20th 2018
Agenda: 7.11.2.2
R4-1805111
Document for: Approval

## Slide 2: Test scope and performance metric
NR PRACH performance metric is the SNR for False alarm probability < 0.1% and Missed detection probability <1%
The requirements on timing estimation error should be further studied

## Slide 3: PUCCH general parameters
NR PRACH performance requirements are defined
  For 1Tx
  For some but not all the supported cell BWs in 38.104
  SCS of 1.5kHz, 5kHz, 15kHz and 30kHz
  Frequency offset of 400Hz

## Slide 4: PRACH format specific parameters
Burst format | SCS(kHz) | Ncs | Logical sequence index | v
0 | 1.25 | 13 | 22 | 32
1 | 1.25 | 0 | 22 | 0
2 | 1.25 | 167 | 22 | 0
3 | 5 | 93 | 22 | 2
A1 | 15 | 2 | 0 | 0
A2 | 15/30 | 10 | 0 | 7
A3 | 15/30 | 27 | 0 | 2
B4 | 30 | 27 | 0 | 2
C0 | 15 | 10 | 0 | 0

## Slide 5: Simulation assumptions
Parameter | Value | Remarks
Number of Tx | 1 | no transparent Tx diversity considered
Number of Rx | 2, 4, 8 | number of diversity branches in baseband
SCS (kHz) | 1.25, 5, 15, 30 | 
channel bandwidth (MHz) | 1.25kHz SCS: 10 5kHz SCS: 10 15kHz SCS: 20 30kHz SCS: 20 | part of the supported BWs is tested
Carrier frequency (GHz) | 4 | 
Burst format | 0, 1, 2, 3, A1, A2, A3, B4, C0 | part of the format is tested
Propagation channel | AWGN, TDL-C (RMS 300ns, UE speed 30km/h) | 
Frequency offset(Hz) | 400 | Assume 0.1 ppm at UE