## Slide 1: WF on UE RF for subPRB R15 feature
Ericsson, Skyworks, Qualcomm
3GPP TSG-RAN4 Meeting #86bis
Melbourne, Australian, 16 April - 20 April 2018
R4-1805140

## Slide 2: Proposals
MPR, A-MPR and IBE will be specified for UE RF spec (36.101)
MPR for CAT-M1
  No MPR needed for 3 & 6 Subcarrier
  2 SubCarrier is to be specified next meeting based on measurement or simulation result
MPR for CAT-M2
  3&6 subcarrier need MPR,
  2 SubCarrier is to be specified next meeting based on measurement or simulation result
MPR table format for CAT M1 and M2:
  the table format to be used in spec is listed in this WF

## Slide 3: Proposal for MPR table for CAT-M2
Channle bandwidth | 15 MHz BW | 
Modulation | BPSK | QPSK
NB index for 2 subcarrier transmission |  | 
MPR |  | 
NB index for 3 subcarrier transmission |  | 
MPR |  | 
NB index for 6 subcarrier transmission |  | 
MPR | ≤ 2 dB | 
Table 6.2.3E-x : Maximum Power Reduction (MPR) for UE category M2 Power Class 3 for subPRB allocation

## Slide 4: Proposal
IBE (working assumption)
  granularity of 3 subcarrier (SubG=3)
  Specify a sub-PRB offset [z] from which the stair case starts
  IBE requirement first step as same as legacy, which is 20log10(EVM)-[x]
  Slew rate step ∆ within the PRB, starting with ∆ =y.
    For the RAN87 meeting consider x=[3], y =[5] and z =[0]
Company are encouraged to provide the simulation result and/or measurement result for the RAN#87 meeting for IBE requirement setting

## Slide 5: Proposal
A-MPR simulation and measurement
  <= 1GHz band, -28 dBc carrier leakage and IQ image
  > 1GHz band, -25 dBc carrier Leakage and IQ image
A-MPR for CAT-M1 to be simulated/measured:
  NS4, NS6, NS12, NS35 and NS38
A-MPR for CAT-M2 to be simulated/measured:
  NS3, NS4, NS5, NS6, NS7,NS12, NS15, NS16 and NS38
A-MPR for other NS value also welcome to be simulated/measured.
Company are encouraged to submit CR for A-MPR and MPR to finalize subPRB feature in RAN4 work