## Slide 1: 3GPP TSG-RAN WG4 Meeting #86Bis Melbourne, Australia, 16 - 20 Mar 2018
Huawei, HiSilicon, Ericsson, …
Way forward on UE performance requirements for eFeMTC
R4-1805476

## Slide 2: Test purpose
Verify the following features for Cat-M1/M2 UE with 1 Rx
  Downlink demodulation performance supporting 64QAM
  CQI reporting based on 64QAM-enabled CQI table
  Demodulation performance under the propagation condition with higher Doppler spread
  Demodulation performance under CRS muting
FFS verification of the following features
  Flexible PDSCH resource allocation
FFS for applicability for non-BL UE supporting coverage enhancement

## Slide 3: New UE performance requirements
  No additional MPDCCH demodulation performance requirement is needed
  Introduce demodulation performance requirements to verify the support of DL 64QAM
  Introduce CQI reporting requirements under 64QAM-enabled CQI table
  Introduce demodulation requirements under CRS muting
  Introduce demodulation requirements for CE mode A UE under Doppler frequency
    200 Hz
FFS
  PBCH demodulation performance requirement
  Possible combinations to reduce number of test cases