## Slide 1: 3GPP TSG-RAN WG4 Meeting #86Bis Melbourne, Australia, 16 - 20 Mar 2018
Huawei, Ericsson, Nokia
Way forward on sTTI BS demodulation requirements
R4-1805494

## Slide 2: SPUSCH
DMRS pattern
  Option 1: “RDD DD DD RD DD RDD”
  Option 2: “RDD DD|R RD DD|R RD RDD”
The DMRS pattern will be decided in the next meeting

## Slide 3: SPUSCH
The 16QAM with ¾ code rate is taken as baseline for SPUSCH FRC (The details are attached in the next slides)
  If any problem is identified for this FRC setup, the FRC may be revisited

## Slide 4: SPUSCH-FRC
Reference channel | A4a-1 |  |  | A4a-2 |  | A4a-3 |  | A4a-4 | 
Allocated resource blocks | 24 |  |  | 48 |  | 72 |  | 100 | 
DFT-OFDM Symbols per subframe | 1 | 2 |  | 1 | 2 | 1 | 2 | 1 | 2
Modulation | 16QAM |  |  | 16QAM |  | 16QAM |  | 16QAM | 
Code rate | 3/4 |  |  | 3/4 |  | 3/4 |  | 3/4 | 
Payload size (bits) | 872 |  | 1736 | 1736 | 3496 | 2536 | 5160 | 3624 | 7224
Transport block CRC (bits) | 24 |  | 24 | 24 | 24 | 24 | 24 | 24 | 24
Code block CRC size (bits) | 24 |  | 24 | 24 | 24 | 24 | 24 | 24 | 24
Number of code blocks - C | 1 |  | 1 | 1 | 1 | 1 | 1 | 1 | 2
Total number of bits per sub-frame | 1152 |  | 2304 | 2304 | 4608 | 3456 | 6912 | 4800 | 9600
Total symbols per sub-frame | 288 |  | 576 | 576 | 1152 | 864 | 1728 | 1200 | 2400

## Slide 5: PUCCH
SPUCCH test setup:
  In SPUCCH demodulation test, use 3 bits per 2 PRB allocation for PUCCH format 4.
  In the test:
    DTX to ACK probability that shall not exceed 1%
    ACK missed detection probability that shall not exceed 1% at the given SNR requirements for sPUCCH performance requirements.
    How to formulate the above metric in the specification, follows the legacy way.