## Slide 1: Wayforward on 1 symbol GP
Mediatek, Intel
3GPP TSG-RAN WG4 RAN#86 Bis
Melbourne, Australia, April 16th- 20th, 2018
R4-1805534
Document for: Approval

## Slide 2: Background: online agreements in RAN4#86 meeting
It is common understanding it is not feasible to support 1-symbol GP for 120khz for FR2 and 60khz for FR1 according to current TA offset design. RAN4 can further disucss the solutions to enable this feature. If no consensus reached, this feature will not be supported in Rel-15
Capability signalling type for 1-symbol GP for 120KHz SCS in unpaired spectrum will be type 4 for FR2. RAN4 will further discuss whether it is feasible to support this feature or not in Rel-15.
Capability signalling type for 1-symbol GP for 60KHz SCS in unpaired spectrum will be type 4 for FR1. RAN4 will further discuss whether it is feasible to support this feature or not in Rel-15.
Feature group
Feature group | Components | Prerequisite feature groups | Need for gNB to know… | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-symbol GP in unpaired spectrum | 1) Slot formats with 1-symbol GP(s) for 120KHz SCS in unpaired spectrum in FR2 2) Slot formats with 1-symbol GP(s) for 60KHz SCS in unpaired spectrum in FR1 |  | Yes | UE does not support 1 symbol GP in unpaired spectrum | Type 4 if needed | Applicable only to TDD | Yes |  | RAN4 will further discuss whether it is feasible to support this feature or not in Rel-15. | RAN4 | TBD | 

## Slide 3: Background: online agreements in RAN4#86b meeting
TA_offset is not tightened in Rel-15

## Slide 4: Wayforward
It is not feasible to support the features of 1 symbol GP for 60KHz in FR1 and 120KHz in FR2 in Rel-15
LS to RAN2 to remove the features from the feature list in Rel-15
  FFS on how to handle later releases
LS to RAN1 on
  The infeasibility of 1 symbol GP for 60KHz in FR1 and 120KHz in FR2 in Rel-15
  The feasible GP length, at least given by
    TAmax is max timing advance value based on expected cell size
    TUE RX-TX is addressed in another separate LS to RAN1 (R4-1805766)
    TA offset can be referred to TS38.133 Table 7.1.2-2