## Slide 1: WF on collision issue among RLM-RS, SMTC and measurement gap
NTT DOCOMO
3GPP TSG-RAN WG4 #86bis
Melbourne, Australia, April 16th - April 20th, 2018
R4-1805541
Document for: Approval

## Slide 2: Background
Following measurement types and scenarios were summarized in agreed WF [1].
FFS which scenario shall be specified and UE behavior in corresponding scenario.
All the UE activities for consideration (all the activities are SSB based)
  RLM
  Measurement type A: Intra-frequency measurement w/o MG and w/o interruption
    For FR1, no mixed numerologies is assumed for this measurement type
    For FR2, this measurement type is not applicable
  Measurement type B: intra-frequency measurement with interruption
    For FR1, mixed numerologies is assumed for this measurement type
    For FR2, Rx beam sweeping is assumed for this measurement type
  Measurement type C: intra-frequency measurement with MG
    E.g. Intra-frequency measurement outside active BWP
  Measurement type D: inter-frequency measurement and inter-RAT measurement
  All the scenarios for consideration
    Fully overlapped scenarios:
      Scenario 1a: Fully overlapped between MG and SMTC in type A
      Scenario 1b: Fully overlapped between MG and SMTC in type B
      Scenario 1c: Fully overlapped between MG and RLM
    Partial overlapped scenarios:
      Scenario 2a: Partial overlapped between MG and SMTC in type A
      Scenario 2b: Partial overlapped between MG and SMTC in type B
      Scenario 2c: Partial overlapped between MG and RLM
    Fully non-overlapped scenarios:
      Scenario 3a: Fully non-overlapped between MG and SMTC in type A
      Scenario 3b: Fully non-overlapped between MG and SMTC in type B
      Scenario 3c: Fully non-overlapped between MG and RLM

## Slide 3: Agreements: UE behavior in case of RLM
Scenario 1c (Full overlap between MG and RLM) is not specified according to agreement in RAN4 #86.
For FR1,
  Scenario 2c/3c (Partial overlap/full non-overlap between MG and RLM)
    All MGs are used for RRM measurements.
    RLM requirements should be specified irrespective of SMTC occasion.
    RLM requirements only consider all the RLM-RS which is not overlapped with MG.
For FR2,
  Scenario 2c/3c (Partial overlap/full non-overlap between MG and RLM)
    All MGs are used for RRM measurements.
    Partial overlap between SMTC and RLM-RS outside of MG
      RLM requirements only consider all the RLM-RS which is not overlapped with SMTC window.
    Full overlap between SMTC and RLM-RS outside of MG
      RLM requirements consider SSB timing sharing between RLM and intra-freq measurement.
        Certain ratio between RLM and intra-freq measurement within available SSB timings should be specified in TS 38.133.
          Value of sharing ratio is TBD.

## Slide 4: Agreements: UE behavior in case of type A/B measurements
For FR1,
  Scenario 1a/1b (Full overlap between MG and SMTC in type A/B)
    UE requirement should be specified for 1a/1b.
      The exact gap sharing between type A/B/C, type D is TBD.
  Scenario 2a/2b (Partial overlap between MG and SMTC in type A/B)
    Type A/type B measurement should only be conducted outside the MG.
    All MGs are used for Type C/Type D measurements.
  Scenario 3a/3b (Full non-overlap between MG and SMTC in type A/B)
    Requirements on type A/B measurement are specified without considering MG.
For FR2,
  Scenario 1b (Full overlap between MG and SMTC in type B)
    UE requirement should be specified for 1b.
      The exact gap sharing between type B/C, type D is TBD.
  Scenario 2b (Partial overlap between MG and SMTC in type B)
    UE behavior on SMTC overlapped with MG would be following options.
      Option 1-1 : Intra freq measurement could be conducted only outside of MG.
      Option 1-2 : Intra freq measurement could be conducted both inside and outside of MG.
  Scenario 3b (Full non-overlap between MG and SMTC in type B)
    Requirements on type B measurement are specified without considering MG.

## Slide 5: Agreements: UE behavior in measurement gap
For FR1,
  Gap sharing among type A/B/C and type D is needed in case of scenario 1a/1b.
  How to share gap timings among each measurements should be determined in RAN4 #87 from options in the next page.
For FR2,
  Gap sharing among type B/C and type D is needed in case of scenario 1b.
  Whether gap sharing is needed in case of scenario 2b would be depending on approved option (option 1-1 or option 1-2) in scenario 2b for FR2.
  How to share gap timings among each measurements should be determined in RAN4 #87 from same options for FR1.
Clarification on Type C measurement
  For intra-frequency measurement, as long as BWP is switched to not cover the intra-frequency target cell SSB frequency during the measurement period, this measurement shall be considered as intra-frequency measurement with gap(type C).

## Slide 6: Agreements: UE behavior in measurement gap
Gap sharing
  Gap sharing among type A/B/C and type D is defined from following options.
    Option 2-1: Gap sharing factor between intra-freq and inter-freq/inter-RAT measurement via signaling could be applied.
    Option 2-2: Scaling factor could be calculated only with SMTC configurations and number of carriers without signaled gap sharing factor (e.g. R4-1804608).
    Other options would not be preclude.

## Slide 7: Reference
[1] 3GPP, R4-1801829, Intel, et al., “Wayforward on UE measurement gap for NR,” Feb. 2018