## Slide 1: Way Forward on NR UE performance requirements
Intel Corporation, Ericsson, Samsung, NTT DOCOMO, Qualcomm, LGE, Spirent
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16 April – 20 April 2018
Agenda Item: 7.11.1
R4-1805549

## Slide 2: NR UE performance requirements
Define the following NR UE performance requirements
  Demodulation performance requirements
    PDSCH (normal demodulation and SDR)
    PDCCH
      At least DL scheduling grant (DCI 1_0 and/or 1_1)
    FFS for PBCH
  CSI reporting requirements
    CQI reporting
    PMI reporting
    RI reporting
    FFS for:
      CRI reporting
      CRI/L1-RSRP reporting
      LI reporting

## Slide 3: NR UE performance requirements
Duplexing mode
  FR1:
    Define both FDD and TDD requirements
  FR2:
    Define TDD requirements only
UE SCS/CBW
  Set of SCS and UE CBW combinations is FFS. The applicable bands are FFS.
  UL/DL configuration for TDD
  Define requirements only for semi-static configuration in Rel-15
  Exact TDD configurations are FFS
  HARQ timing and number of processes is FFS

## Slide 4: NR UE performance requirements
  Number of UE RX ports and MIMO layers
  FR1
    Define 2RX and 4RX ports requirements
    Up to 4 MIMO layers
  FR2
    Define 2RX ports requirements
    Up to 2 MIMO layers
MCS/TBS for PDSCH demodulation
  FR1
    QPSK/16QAM/64QAM/256QAM
  FR2
    QPSK/16QAM/64QAM

## Slide 5: Channel Models
      Propagation channel models for FR1 performance requirements
        Use simplified TR 38.901 TDL channel models
          FFS for power delay profiles
          FFS for Delay spread values
          FFS how to simplify the models
          FFS MIMO antenna correlation models
      Propagation channel models for FR2 requirements
        FFS

## Slide 6: Other open issues (for information)
Common
  RF impairments models (e.g. Tx EVM, RX EVM, phase noise)
  Deployment scenarios
  SA/NSA requirements
PDSCH
  Performance metrics
  FRCs
  HARQ parameters and RV sequence
  Resource allocation
  PRB bundling parameters
  DRMS configuration
  CSI-RS for TRS
  PTRS
  QCL
  Reference receiver assumptions
PDCCH
  Test metrics
  Aggregation level
  CORESET configuration
  DCI format (number of bits)
  Reference receiver assumptions
CQI reporting
  Test metrics
  Wideband/Subband CQI tests
  CQI tables
PMI reporting
  Test metrics
  Wideband/Subband CQI tests
  Number of APs
  Codeebook types
RI reporting