## Slide 1: WF on intra-band B41 EN-DC A-MPR
3GPP TSG-RAN WG4 Meeting #86bis R4-1805645 Melbourne, AU, 16th – 20th April, 2018

## Slide 2: Proposals
A-MPR should be defined for 2PA
Single Switched UL should be supported
  UE SUO bit requires RAN to schedule single UL
  Single UL would use standalone LTE or NR A-MPR
3) A-MPR should first be developed for Type 2 UEs
  Dynamic Power sharing can be addressed in Rel-16
4) A-MPR should be defined to allow for several classes of channel arrangement

## Slide 3: Overview of Architecture Variants
Rel-15 Operation – Static, Based on UE SUO capability |  | 
 | 1PA | 2PA
Single Uplink Operation | UE expected to signal SUO support for the EN-DC band combination. RAN schedules Single Tx. | UE could optionally signal SUO support, and would be scheduled for Single Tx.
Simultaneous Dual Tx | UE could potentially not signal SUO support, but would be required to operate with A-MPR defined for 2PA. | A-MPR to be defined for this case.

## Slide 4: Single Switched UL
Single Switched UL should be supported
  Two Options for TDM
    Option 1: UL TDM pattern as per R4-1805323
    Option 2: UL TDM based on LTE eIMTA framework, to reserve subset of the available UL subframes for LTE.
  UE signal of support for SUO for a given EN-DC band combination obligates RAN to configure single switched uplink for that EN-DC band combination
  No additional signaling required
For Rel-16, rules/mechanisms can be developed to allow dynamic or semi-static switching between Single Uplink and Dual Tx

## Slide 5: EN-DC A-MPR Definition
EN-DC A-MPR should be defined for a reference architecture of 2PA
  Specification of A-MPR for 1PA is not needed in Rel-15
A-MPR should be defined for Type 2 UEs, where each RAT assumes worst case allocation (1RB, full power) on other RAT
EN-DC AMPR should be defined as MAX of A-MPR for two components:
  Single Channel MPR and A-MPR defined in 36.101 and 38.101-1
  A-MPR for EN-DC, which covers IMD products and ACLR
A-MPR for Type 1 UEs could also be defined if time permits.

## Slide 6: EN-DC A-MPR definition (cont.)
allocation size
AMPR allowed
A-MPR should be defined as formula primarily based on allocation size.
Approach similar to LTE MPR definition for non-contiguous allocations
Details of formula can be decided in next meeting.
Separate curves will be defined for different channel arrangements
Curve 1 - -13 dBm/1MHz limit
  Contiguous channels – high channels where no IM3s in NS_04 spurious
  Non-contiguous channels – where all IM3s fall into regions with filter attenuation > 12 dB
Curve 2 - -25 dBm/1MHz limit
  Other channel allocations – some IM3s fall into spurious regions without filter attenuation

## Slide 7: Assumptions for A-MPR definition
2PA Architecture
  [X] dB post-PA insertion loss on each Tx chain
  [Y] dB antenna isolation
A-MPR allowance is defined per Tx, and is MAX of AMPR for two components:
  Single Channel MPR and AMPR defined in 36.101 and 38.101-1
  AMPR for EN-DC, which covers IMD products and ACLR
A-MPR for EN-DC based on PC2, also applies to PC3
A-MPR for EN-DC to be developed for DFT-S-OFDM
  Definition for CP-OFDM is second priority and can be defined if time allows