## Slide 1: WF on TDD configuration for NR UE REFSENS
NTT DOCOMO, INC., …
R4-1805717
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16-20 April 2018
Agenda Item: 7.4.10

## Slide 2: Background
At the RAN4 #86, the WF on TDD configuration for NR REFSENS was agreed
  R4-1803445 “Way forward on NR UE REFSENS IM and FRC”, Huawei, HiSilicon, Intel, Samsung, Qualcomm
Based on above WF, at the RAN4 #86bis, TDD configuration for NR REFSENS was discussed in the following contributions.
  R4-1804978, Consideration on NR TDD configuration, DOCOMO Communications Lab.
  R4-1804102, NR UE REFSENS SNR, Qualcomm Incorporated
  R4-1804155, NR UE REFSENS SNR, Intel Corporation
  R4-1804563, Discussion about NR UE REFSENS requirements, LG Electronics Inc.
  R4-1805316, Discussion on FRC for NR UE REFSENS, Huawei, HiSilicon
This document summarizes the Agreements on TDD configuration for NR REFSENS

## Slide 3: Agreements for FR1 and FR2
The following parameters need to be decided by RAN4 #87 to finalize reference measurement channel for NR REFSENS
  TDD configuration (UL/DL pattern)
  DL HARQ timing related parameters (K0, K1)
  Max number of HARQ process

## Slide 4: Agreements for FR1
For FR1, the following TDD/HARQ configurations are applied for NR REFSENS requirements
  Semi-static TDD configuration
  UL/DL pattern
    FFS: TDD configuration for LTE side in EN-DC combinations (whether to apply the same configuration as NR side)
    FFS: Different TDD pattern between EN-DC and other scenario
  K0 = [0]
    FFS: K1 and max number of HARQ process
SCS | Alt.1 | Alt.2 | Alt3 | Alt4
15kHz | Aligned with LTE config #2 (5ms periodicity) |  |  | 
30kHz | {0, 33, 0, 41} (Option 3 in R4-1803445) | Aligned with LTE config #2 (5ms periodicity) | {0 0 0 32 1} with 2.5ms periodicity | {0 0 0 12 1} with 2.5ms periodicity
60kHz | {0, 33, 0, 41} (Option 3 in R4-1803445) | Aligned with LTE config #2 (5ms periodicity) | LTE config #2 with 1.25ms periodicity | {0 0 13 1} with 1ms periodicity

## Slide 5: Agreements for FR2
For FR2, semi-static TDD configuration
Postpone the discussion for FR2 to RAN4 #87
K0 = [0]
  FFS: K1 and max # of HARQ process