## Slide 1: WF on NR intra-band contiguous UL CA in n257
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16 - 20 Apr 2018
R4-1805730

## Slide 2: Background
Considering Rel-15 schedule, it is proposed in [1] to
  Specify Intra-band contiguous NR UL CA in n257 with maximum aggregated BW up to 400 MHz (i.e. 200x2) with only contiguous resource allocation in Rel-15
  Use the same MPR as that of 400 MHz single-carrier
On the other hand, MPR is provided in [2] for
  Contiguous Allocations with aggregated BW up to 800 MHz
    For aggregated BW <= 200 MHz, the same MPR as that of single-carrier <= 200 MHz is proposed
    For aggregated BW > 200 MHz and <= 600 MHz, the same MPR as that of single-carrier of 400 MHz is proposed
  Also, Non-Contiguous Allocations with aggregated BW up to 800 MHz
Only this gap is allowed
Contiguous allocation across CCs
200 MHz
200MHz
Same OFDM type

## Slide 3: Way forward
To confirm if the MPR proposed in [2] is applicable for NR intra-band contiguous UL CA in n257 for the next meeting considering;
  PAPR difference between single-carrier and intra contiguous UL CA for both DFT-s-OFDM and CP-OFDM
  Impact of gap between CCs due to nominal channel spacing.
    Allowed ratio of (allocation RB BW)/(gap BW) must be studied to ensure MPR is comparable to CP-OFDM MPR in [2]
  Case when different waveforms (DFT-s-OFDM and CP-OFDM) are in different CCs.
If it is applicable, those intra-band contiguous CA scenarios described in [2] in n257 is specified in RAN4#87
If not applicable, at least the following requirements in n257 are specified with necessary modifications to MPR proposed in [2]
  Maximum aggregated BW up to 400 MHz (i.e. 200x2 MHz)
  Only contiguous resource allocation (gap between CCs due to nominal channel spacing is allowed)
The MPR could be revisited once the CA FR2 EVM, IBE, SEM and ACLR are finalized
Mandatory CBW for single-carrier in FR2

## Slide 4: Reference
[1] R4-1804365, Intra-band contiguous NR UL CA in FR2 in Rel-15, NTT DOCOMO, INC.
[2] R4-1805181, FR2 CA MPR, Qualcomm Incorporated