## Slide 1: WF on intra-band B41 EN-DC A-MPR
3GPP TSG-RAN WG4 Meeting #86bis R4-1805774 Melbourne, AU, 16th – 20th April, 2018

## Slide 2: Proposals
A-MPR should be defined for 2PA with 2 antennas
Single Switched UL is allowed as a per-BC UE capability
3) A-MPR should first be developed for Type 2 UEs
  A-MPR for Type 1 UEs should be completed if possible
4) A-MPR should be defined to allow for several classes of channel arrangement
5) The agreement applies only to B41/n41
6) Band Combination can be considered complete even if A-MPR definition is not completed

## Slide 3: Overview of Architecture Variants
Rel-15 Operation – Static, Based on UE SUO capability |  | 
 | 1PA | 2PA
Single Uplink Operation | UE would signal SUO support for the EN-DC band combination. UE expects RAN to schedule Single Tx. | UE could optionally signal SUO support, and would be scheduled for Single Tx.
Simultaneous Dual Tx | UE could potentially not signal SUO support, but would be required to operate with A-MPR defined for 2PA. | A-MPR to be defined for this case.

## Slide 4: Single Switched UL
Single Switched UL is allowed
  Multiple Options for TDM – RAN4 may have specific requirements for these options.
    Option 1: UL TDM pattern as per R4-1805323
    Option 2: UL TDM based on LTE eIMTA framework, to reserve subset of the available UL subframes for LTE.
    Option 3: Dynamic UL TDM
    Other options are not precluded.
  As a per-BC UE capability, UE may signal support for SUO for a given EN-DC band combination. If dual transmission is scheduled instead of single switched uplink, UE behavior is unspecified.
  No additional signaling required
For Rel-16, rules/mechanisms could be developed to allow dynamic or semi-static switching between Single Uplink and Dual Tx

## Slide 5: EN-DC A-MPR Definition
EN-DC A-MPR should be defined for a reference architecture of 2PA with 2 antennas
  Specification of A-MPR for 1PA is not needed in Rel-15
A-MPR should be defined for Type 2 UEs, where each RAT assumes worst case allocation on other RAT
A-MPR for Type 1 UEs could also be defined if time permits.

## Slide 6: EN-DC A-MPR definition (cont.)
allocation size
AMPR allowed
A-MPR should be defined as formula primarily based on allocation size.
Approach similar to LTE MPR definition for non-contiguous allocations
Details of formula can be decided in next meeting.
Separate curves will be defined for different channel arrangements
Details and criteria for curve selection can be decided in next meeting

## Slide 7: Assumptions for A-MPR definition
2PA Architecture
  4 dB post-PA insertion loss on each Tx chain
  10 dB antenna isolation
A-MPR allowance should be applied equally to both LTE and NR in Type 1 UEs
A-MPR for EN-DC based on PC2, also applies to PC3
A-MPR for EN-DC to be developed for DFT-S-OFDM
  Definition for CP-OFDM is second priority and can be defined if time allows
Assumption for A-MPR should be equal PSD between channels