## Slide 1: WF for CA ACS BW
3GPP TSG-RAN WG4 Meeting #86bis R4-1805784 Melbourne, AU, 16th – 20th April, 2018
Qualcomm, Inc.

## Slide 2: Background
Companies have provided their views on CA ACS level based on previous agreement [1], where the jammer BW was the sum of the component carrier BW's.
Intel [2] proposed 16dB relaxation ACS level to ensure ACS jammer <= IBB1 jammer level based on [1]
Huaweii [3] proposed 3dB relaxation on ACS level based on [1] regardless of CA BW, and they proposed that using jammer BW for CA > 2CC is FFS.
Qualcomm [4] proposes to revise it's own working agreement by providing 2 options for Jammer BW for CA ACS with ACS level of [33] – 10*log(Agg_BW/100M) for the fixed jammer BW; per DoCoMo old paper [5].
  Example. CA BW = 110M, ACS level ~ 33dB
  Example CA BW = 200M, ACS level ~ 30dB
Qualcomm has the following concern on excessive jammer BW are as follows:
-The typical blocker BW in NR bands from gNB will vary from 50M to 100M.
-When close to gNB, the blocker BW (50M-100M) will dominate.
-Excessive Relaxation of ACS level will compromise system performance

## Slide 3: WF
Encourage companies to evaluate and study ACS level for fixed jammer BW of 100MHz
The target ACS level is [33] – 10*log(Agg_BW/100M).
Supporting Operators for 100MHz fixed jammer BW are DoCoMo, KDDI, and Softbank

## Slide 4: References
[1] R4-1802267, “2DL/1UL intra-band contiguous NR CA ACS, IBB for NR bands in Sub 6”, Qualcomm Incorporated.
[2] R4-1804141, “ACS and IBB requirements for 2DL/1UL intra-band contiguous CA ”, Intel Corporation.
[3] R4-1804443, “Discussion of sub-6 intra-band contiguous CA ACS/IBB requirement ”, Huawei, HiSilicon.
[4] R4-1802267, “2DL/1UL intra-band contiguous NR CA ACS, IBB for NR bands in Sub 6”, Qualcomm Incorporated.
[5] R4-1800255, “CA configuration agnostic RF requirements for 2DL/1UL intra-band contiguous NR CA for NR bands in FR1”, NTT DOCOMO, INC..