## Slide 1: WF on FR2 DL 256QAM
NTT DOCOMO, INC., Nokia, Huawei, CMCC, KDDI, AT&T, Orange, Verizon, Deutsche Telekom, Vodafone, China Telecom, KT, Etisalat, SK telecom…
R4-1805882
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16-20 April 2018
Agenda Item: 7

## Slide 2: Background
256QAM for FR2 was discussed in the following contributions.
  R4-1804171 Views on NR FR2 256QAM requirements Intel Corporation
  R4-1804987 On EVM Requirement for FR2 Ericsson
  R4-1803717 On 256QAM for FR2 CATT
  R4-1803934 Consideration on 256QAM support for FR2 Huawei, HiSilicon
  R4-1805337 256QAM EVM for FR2 NR BS NTT DOCOMO, INC.
  R4-1804958 EVM requirements for BS type 2-O Nokia, Nokia Shanghai Bell
This document summarizes the Agreements/WF on introduction of 256QAM for FR2

## Slide 3: Agreements
In Rel-15, introduce 256QAM BS Tx EVM requirement in core spec 38.104. Required EVM value is [3.5%].
  It is noted that the value [3.5%] may be reconsidered/revisited in later Release based on the detail analysis in RAN4.
  [3.5%] EVM is staring point. In RAN4#87 meeting, decide the final value.
Not to introduce UE RX requirements (RF and/or perf) in Rel-15.
FFS how to introduce 256QAM related UE Rx requirements (RF and/or perf) in later release.
Notes: DCM: We can have this as optional feature.
QC: For same balance, who brings analysis?
Ericsson: Optionality is not issue. Whether to introduce the requirements for 256QAM
HW: This is compromise solution. UE couldn’t implement and tested, we have capability. But for CPE. we can test and use 256QAM.
Samsung: What does means same balance?
Intel: Same view as QC. No analysis for same balance. Any companies have not shown the benefit of 256QAM. Power offset is needed, and it brings coverage reduction. In LTE, RAN1 performed much system level analysis and showed the gain.
ZTE: We need to define the requirements considering technical issues.
Ericsson: HW and Nokia's link analysis is not realistic since ideal compensation is assumed. No company show system level analysis.
Nokia: PA compression is not technical issue. Coverage can be kept.
Samsung: Increase of Tx offset loses Tx opportunity.
DCM: In LTE, BS can reduce Tx power. We can take same approach. Tx offset value is not specified in the specs.
Ericsson: Coverage is shrined in FR2
QC: To define BS requirements means to define UE requirements automatically.
Ericsson: Benefit is questionable.
HW: In our analysis, we use phase noise model captured in TR.
Nokia: Phase noise is implementation dependent.
MTK: Why we need to introduce 256QAM rashly. We don't have much time for Rel.15. Many venders find the feasibility issue. And a lot of remaining issue.
DCM: It is not new issue, we had discussion since last year. RAN4 agreed that Feb is deadline, but we don't have consensus. Question is, there was a comment Feb was a limit for HW implementation, but not only 256QAM but also other RF requirement is not finalized yet. It will also impact HW implementation.
Samsung: For same balance, there is no response to clarity the meaning. To show the benefit, we need to use the same assumption.
Nokia: It is possible to provide the benefit assuming the same assumption.
HW: 3.5% is already used in LTE. This provided the same balance between BS and UE
Ericsson: in LTE, FR1 is assumed.
HW: For FR2, BS has more flexibility to implement this feature.
Ericsson: We need to be carefully for FR2.
ZTE: We should not have any conclusion without technical analysis.
-> continue offline and coffee break session in Thr. evening.