## Slide 1: WF on UE capability clarification for simultaneous RxTx for NR
CMCC, Ericsson, Orange, Vodafone, KDDI, China Telecom
3GPP TSG-RAN WG4 Meeting #86bis R4-1805925
Melbourne, Aus, 16-20 Apr, 2018

## Slide 2: Background
In RAN4#86 meeting, RAN4 has reached some agreements on simultaneous RxTx capability for NR UE:
  For Simultaneous reception and transmission for inter-band CA or EN-DC, the capability signalling is per band combination. Whether to mandating this feature in certain band combinations will FFS
  Split the feature 2-4 into EN-DC and NR-CA. Type 3 capability signalling (per band combination) is applied for both EN-DC and NR-CA. Further discuss in RAN4 86bis whether to mandate this feature for both EN-DC and NR-CA

## Slide 3: Agreements (1/2)
  Simultaneous RxTx is a band combination specific UE capability for EN-DC and NR CA (for both TDD-TDD and TDD-FDD combinations) and it can be either mandatory or optional.
    RAN4 will agree on band combinations on which the capability can be made mandatory and on which the capability will be optional.
  Band combinations for simultaneous RxTx from operators should be added in slide5
  Companies are encouraged to calculate MSD due to the simultaneous RxTx capability for per band combinations in RAN4#87 meeting.

## Slide 4: Agreements (2/2)
Procedure for discussions on band combinations for this capability
  Operators are encouraged to propose band combinations for which mandatory simultaneous RxTx capability is requested
  Relevant ΔTib/ΔRib and MSD (if needed) will be discussed based on submitted contributions in RAN4#87.
RAN4 to specify in 38.101 the band combinations for which simultaneous RxTx capability can be made mandatory for inter-band CA or EN-DC combinations
  A big CR will be proposed in RAN4#87 meeting capturing all relevant band combinations
  Request for band combinations with mandatory simultaneous RxTx capability can be introduced in Rel-15 in release independent manner.

## Slide 5: Some criteria
Simultaneous RxTx can be mandatory by following some general criteria as listed below:
  For TDD-FDD combinations, the capability shall be mandatory if low-band (below 1GHz) is aggregated with high (i.e. 2.69GHz and above) and mid-band (1GHz to 2.69GHz) TDD cells
  The capability shall be FFS if mid-band (1GHz to 2.69GHz) FDD is aggregated with high (i.e. 2.69GHz and above) TDD cells.
  For TDD-FDD combinations in high FDD bands, the capability is FFS.
  For TDD-TDD combinations between mid-band and high band, the capability can be mandatory.
  For TDD-TDD combinations in high bands, the capability is FFS.

## Slide 6: Requested combinations for simultaneous TX/RX(Example)
Band combination | Simultaneous RxTx UE capability | Request from operators
CA_n39A-n78A | mandatory | CMCC
DC_39A-n79A | mandatory | CMCC
Operators are encouraged to propose relevant combinations for this capability

## Slide 7: References
  [1] R4-1803857 Discussion on NR UE capability clarification for simultaneous RxTx CMCC
  [2] R4-1804011Further discussions on UE capability clarification for simultaneous RxTx for NR Ericsson
  [3] R4-1803551 WF on UE feature list for CA/EN-DC, other capability and LTE-NR co-existence