## Slide 1: WF on How to Distinguish UE Types in FR2
Samsung, LGE, Intel, Verizon …
R4-1805926
3GPP TSG-RAN WG4#86-Bis Meeting
Melbourne, Australia, April 16-20, 2018
Agenda: 7.4.7.1

## Slide 2: Background
Several UE types in FR2 have been identified previously
Current 38.101-2 specifies EIRP and TRP only for Handheld UE
FWA has been discussed recently and will most likely have different requirements for min peak EIRP, min peak EIS and spherical EIRP/EIS from those of Handheld UEs
Discussions on desired applications highlighted some key differences between potential UE types
  Though FCC uses mobile and transportable terms, transportable refers only to max EIRP of 55 dBm and excludes FWA devices on a moving platform

## Slide 3: Way forward
Consider min peak EIRP level, spherical coverage needs as potential distinguishing factors between UE types (other aspects are not precluded)
  Priority is to finalize the previously discussed and approved handheld UEs (#1) and FWA on a stationary platform (#4), whose target is Rel-15
  Companies are encouraged to submit contributions explicitly discussing the specific requirements for #2 and #3
    RAN4 should discuss how to move forward with types that are not completed in Rel-15 scope
      Release independent approach
    The table below captures all the types discussed so far. It will be revised as new contributions are discussed and requirements are clearer
# | Min Peak EIRP (dBm) | Spherical coverage | Maximum allowed EIRP (dBm) | Maximum allowed TRP (dBm) | Comments*
1 | [22.0-22.4] | Full sphere | 43 | 23 | Handheld UE
2 | [26-30] | Half sphere | 43 | 23 | Vehicle mounted UE (fixed on moving platform)
3 | [~35] | Full sphere | 43 | 23 | Higher power mobile UE
4 | [30-40] | Half sphere or further limited sphere | 55 | 35 | FWA on fixed platform
NR FR2 UE Type summary
*Note: these notes are meant to illustrate examples that have the requirements listed, other examples are not precluded