## Slide 1: Summary of network performance analysis for spherical coverage
Samsung
R4-1805930
3GPP TSG-RAN WG4#86b Meeting
Melbourne, Australia, Apr 16 – 20, 2018
Agenda: 7.4.8.3.2

## Slide 2: Evaluation assumptions
Assumptions as agreed in R4-1801198 & R4-1803275. Differences in reference and evaluated spherical coverages are shown below
 | Apple/Intel (R4-1802220) | Qualcomm (R4-1805669) | Samsung (R4-1803820) | MediaTek (R4-1804412) | LGE (R4-1804489)
UL peak EIRP (dBm) | 22 | 22.5 | 22.4 | 22 | 21.5
Reference spherical coverage (Ref) | TR -5dB@50%tile -10dB@20%tile | TR CFG -5.6dB@50%tile -11.7dB@20%tile | TR (finite beam points) -5dB@50%tile -10dB@20%tile | TR CDF model -5dB@50%tile -10dB@20%-tile | TR CDF model -5dB@50%tile -10dB@20%-tile
Evaluated spherical coverage (Eval) | “Model 2 (A+B)” (2-panel, same side) -11.5dB@50%tile -17.7dB@20%tile | “CFG1” (1 panel) -11.7dB@50%tile -18.4@20%tile | Assumption 1 -8.6dB@50%tile -15dB@20%tile | Assumption 3 -11.6dB@50%tile -13.5dB@20%tile | -12.5dB@50%tile -18.5dB@20%tile
UE orientation | Uniform on sphere surface | EL: U(0:180); Az: U(0:360) | EL: U(0:180); Az: U(0:360) |  | 
Samsung
Qualcomm
Apple/Intel
LGE

## Slide 3: Summary of outage evaluation results
Outage evaluation results submitted to RAN4#86b
Outage (UL 20MHz) | Peak EIRP | UMa (0% indoor) |  | UMa (20% indoor) |  | UMa (100% indoor) |  | Dense urban (0% indoor) | Dense urban (20% indoor) | Dense urban (100% indoor) | InH | Remark
 |  | ISD 200m | ISD 400m | ISD 200m | ISD 400m | ISD 200m | ISD 400m |  |  |  |  | 
Apple/Intel (R4-1805381) | 22 dBm | 0% | 4% | 6% | 15% | 39% | 63% | 0% | 5% | 25% | 0% | TR + mask
LGE (R4-1804489) | 21.2 dBm | 0.3% | 2.5% |  |  |  |  | 0.1% |  |  | 0.4% | 
 | 23.2 dBm | 0.2% | 1.6% |  |  |  |  | 0.06% |  |  | 0.4% | 
Samsung (R4-1803820) | 21.2 dBm | 0.1% | 1.3% | 7.8% | 14.8% | 37.4% | 66.1% | 0% |  |  | 0% | UE assumption 1
 | 22.4 dBm | 0.0% | 1.0% | 7.2% | 13.8% | 35.0% | 63.2% | 0% |  |  | 0% | 
 | 23.2 dBm | 0.0% | 0.9% | 6.7% | 13.3% | 32.6% | 61.1% | 0% |  |  | 0% | 
MediaTek (R4-1804412) | 22 dBm | 0% | 3.2% |  |  |  |  |  |  |  | 0% | Specific CDF model

## Slide 4: Summary of throughput evaluation results - 1
Mean throughput evaluation results submitted to RAN4#86: loss compared to respective reference spherical coverage
  No hand/body losses or other blockages is considered in the analysis. It is not necessary if evaluation assumes at least one antenna array is not blocked
Mean throughput loss |  | Urban macro (0% indoor) |  | Dense urban (0% indoor) | Indoor hotspots
 |  | ISD 200m | ISD 400m |  | 
Apple/Intel (R4-1805381) | DL | <0.5% | 3% | <1% | <1%
 | UL | 13% | 12% |  | 
Qualcomm (R4-1804660) | DL | 4.6% | 9.9% | 7.1% | 11.5%
 | UL | 18.5% | 20.3% | 9.6% | 7.9%
Samsung (R4-1803820) | DL | 6.62% | 11.05% | 6.10% | 7.28%
 | UL | 5.51% | 7.58% | 7.61% | 5.10%
MediaTek (R4-1804412) | UL | 7.3% | 11.2% |  | 2.9%
LGE (R4-1804489) | UL | 5.7% | 13.7% | 1.4% | 3.4%

## Slide 5: Summary of throughput evaluation results - 2
5%-tile throughput evaluation results submitted to RAN4#86: loss compared to reference spherical coverage
Note: The evaluation is for full buffer traffic and round-robin scheduler.
5%-tile throughput loss |  | Urban macro (0% indoor) |  | Dense urban (0% indoor) | Indoor hotspots
 |  | ISD 200m | ISD 400m |  | 
Qualcomm (R4-1804660) | DL | 16.9% | 30.1% | 23.1% | 26.4%
 | UL | 56.8% | N.A. | 33.5% | 30%
Samsung (R4-1803820) | DL | 27.83% | 19.87% | 28.00% | 21.74%
 | UL | 15.53% | 3.90% | 23.26% | 20.05%

## Slide 6: Network Performance Sensitivity to EIRP CDF
Source | Deviation from a ref |  | UL throughput loss wrt TR model |  | Remark
 |  |  | Mean | 5%-tile | 
Apple/Intel (R4-1805381) | 50%-tile | -8dB |  | > 25% | Ref for deviation is TR model
 | 20%-tile | -8dB |  | 10% | Ref for deviation is TR model
Qualcomm (R4-1805669) | 50%-tile | -8dB | 18% | 60% | Ref for deviation is TR model
 | 20%-tile | -8dB | 5% | 26% | Ref for deviation is TR model
Samsung (R4-1803820 rev) | 20%-tile | -5dB | 1.49%, |  | Ref for deviation is Assumption 1
 |  | 0dB | 5.51% |  | 
 |  | +5dB | 8.74% |  | 
Apple/Intel (R4-1805381)
Samsung (R4-1803820 rev)
Qualcomm (R4-1805669)

## Slide 7: Appendix: Assumptions for EIRP CDF
Updated assumptions has been agreed in RAN4 AH-1801
 |  | Assumptions1 | Assumptions2 | Assumptions3 | Assumptions4 | Assumptions5 | Assumptions6 | Assumptions7 | Notes
Frequency range |  | n257 | n257 | n257 | n257 | N257 | n257 | N257 | 
# of antenna in an antenna module/set (# of patches, # of dipoles, etc.) |  | - | - | - | - | - | - | - | Depends on the current implementation
# of antenna module/set in total |  | 1 | 1 | 2 | 2 | 2 | 3 | 3 | 
Finite UV test points | Y/N | Y | Y | Y | Y | Y | Y | Y | Finite test point shall be the baseline
Beam phase shifter controller | degree | 45 | 45 | 45 | 45 | 45 | 45 | 45 | Finite beam shall be the baseline
Antenna type (patch, dipole, or both) |  | - | - | - | - | - | - | - | Depends on the current implementation
Antenna module/set location (front, back, top-side, left-side, right-side, bottom-side) |  | Top / Bottom | Top / Bottom | Top & Bottom | Top & Bottom | Top & Bottom | Left & Right & Bottom | Left & Right & Bottom | combination of the lists are not precluded.
Front cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Glass | Glass | Glass | Glass | Glass | Glass | This information is meaningful only if it’s the same with the material which covers antennas.
Back cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Plastic | Glass | Glass | Plastic | Glass | Plastic | 
Side cover / Frame (Plastic, Glass, Ceramic, Metal) |  | Metal | Plastic | Metal | Metal | Plastic | Metal | Plastic | 
Device size (WxHxD) | cm3 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | This is for information
Display panel – Full (Y) or Partial (N) | Y/N | Y | Y | Y | N | Y | Y | Y | 
Bezel Margin | mm | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | Module can’t be placed outer edge of UE to secure mechanical reliability

## Slide 8: Appendix: Work plan
Initiate offline and email discussion (after RAN4#85) on the use cases and model assumptions for NW performance analysis
RAN4 NR AH #4 (January ’18)
  Initial discussion of simulation results (Both EIRP CDF and Network) based on the harmonized assumptions in this way forward.
  Propose harmonized NW model assumptions and update based on preliminary analysis.
RAN4 #86 (February ’18)
  Deadline to submit the EIRP CDF simulation results based on the harmonized assumptions. Target preliminary EIRP CDF spherical requirement, based on the simulation outcomes.
  Continue to improve the NW simulation accuracy reflecting initial EIRP CDF requirement (from AH #4)
  Initial discussion of measurement results for prototype devices
RAN4 #86bis (April ’18)
  Continue to improve the NW simulation accuracy reflecting preliminary EIRP CDF requirement (#86)
  Continue to improve the prototype measurement effort and compare to preliminary EIRP CDF simulation
RAN4 #87 (May ’18)
  Finalize the spherical coverage requirement for handheld UEs based on the contributions