## Slide 1: Way forward on NSSS based RRM measurement
Huawei, HiSilicon, ….
3GPP TSG-RAN WG4 Meeting #86bis R4-180xxxx
Melbourne, Australia, April 16 – 20, 2018
Agenda Item: 6.17.4.2

## Slide 2: Background
In RAN4 84bis (R4-1711893)
  RAN4 confirms that it is feasible to use NSSS on an anchor carrier for RRM measurement, under the working assumption that the ratio of NSSS EPRE to NRS EPRE is configured from {-3, 0, 3, spare} dB.
  RAN4 identified that the antenna port(s) used for the measurement may vary arbitrarily across subframes and across cells in NSSS, and is still studying the potential impact of such variation.
In RAN4 85 (R4-1714485), RAN4 further clarified that:
  Earlier agreement on the feasibility of NSSS-based RRM measurement is under the assumption that NSSS is always transmitted from Tx port 2000.
  Companies are encouraged to investigate the feasibility of NSSS-based RRM measurement when there are no conditions on the antenna port(s) used for NSSS transmission.

## Slide 3: Agreement
Accuracy requirement and test cases for NSSS-based RRM measurements are defined under the condition that NSSS is transmitted from single Tx antenna port