## Slide 1: Way forward on Scell activation delay
Intel, [], …
R4-1805968
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, AU, 16th – 20th April, 2018
Agenda Item: 7.9.10.3

## Slide 2: SCell activation delay
Background: it was agreed in RAN4#86 that
  Tactivation_time is consisted of
    RF warm up excluding AGC settling: TBD and independent of SCS
    AGC settling: N1(*) SMTC periods for known and N2 SMTC periods for unknown cells
    PSS/SSS and SSB index acquiring:
      X1 SMTC periods for known cell provided that PSS/SSS detection and MIB reading are not needed
      X2 SMTC period for known cell provided that MIB reading is needed
      X3 SMTC period for unknown cell provided that PSS/SSS detection and MIB reading are needed
      X1, X2 and X3 will be decided by RAN4#86bis

## Slide 3: Way forward on the definition of “known” and “unknown”
SCell is known if it has been meeting the following conditions:
  During the period equal to max([5] measCycleSCell, [5] DRX cycles) before the reception of the SCell activation command:
    the UE has sent a valid measurement report,
    the SCell being activated is indicated as a synchronous cell or the UE has already decoded MIB of the target Scell
    the SCell being activated remains detectable according to the cell identification conditions specified in section [TBD],
  the SSB measured during the period equal to max([5] measCycleSCell, [5] DRX cycles) also remains detectable during the SCell activation delay according to the cell identification conditions specified in section [TBD].
When the cell is known, it is FFS on the conditions for the scenario where MIB detection is needed and the scenario where MIB detection is not needed
For FR2 case, Rx beam sweeping is needed regardless the activated SCell is known or unknown

## Slide 4: Way forward on SCell Activation
In addition to agreements in RAN4#86 on Tactivation_time, the UE will also need time to decode the MAC-CE message.
  Companies to investigate how much time is needed for MAC-CE message decode.
SSB based activation delay requirement Tactivation_time in FR1
  Tactivation_time is consisted of
    MAC-CE message decode time
    RF warm up excluding AGC settling: TBD
    AGC settling: N1 SMTC periods for known and N2 SMTC periods for unknown cells
      The exact value of N1 and N2 are TBD
      It is FFS that the parameter value of N1 shall depend on the SCell measurement cycle in use prior to the SCell activation
    PSS/SSS and SSB index acquiring:
      [2] SMTC periods for known cell provided that PSS/SSS detection and PBCH decoding are not needed
      [4] SMTC period for known cell provided that PBCH decoding is needed
      [5] SMTC period for unknown cell provided that PSS/SSS detection and PBCH decoding are needed
SSB based activation delay requirement Tactivation_time in FR2
  Tactivation_time is consisted of
    MAC-CE message decode time
    RF warm up excluding AGC settling: TBD
    AGC settling: N3 SMTC periods for known and N4 SMTC periods for unknown cells
      The exact value of N3 and N4 are TBD
      It is FFS that the parameter value of N3 shall depend on the SCell measurement cycle in use prior to the SCell activation
    PSS/SSS and SSB index acquiring:
      Rx beam sweeping should be considered for PSS/SSS detection and measurement for FR2 for both known and unknown cell
      The corresponding delay is FFS